Subpart D—Standards and Requirements for Project

§39.19  General requirements for site selection and construction of veterans’ cemeteries.

(a) The various codes, requirements, and recommendations of State and local authorities or technical and professional organizations, to the extent and manner in which those codes, requirements, and recommendations are referenced in this subpart, are applicable to grants for construction of veterans’ cemeteries. Additional information concerning these codes, requirements, and recommendations may be obtained from the Department of Veterans Affairs, National Cemetery Administration, 810 Vermont Avenue, NW., Washington, DC 20420.

(b) The standards in §§39.19 through 39.22 constitute general design and construction criteria and shall apply to all projects for which Federal assistance is requested under 38 U.S.C. 2408.

(c) In developing these standards, no attempt has been made to comply with all of the various State and local codes and regulations. The standards contained in §§39.19 through 39.22 shall be followed where they exceed State or local codes and regulations. Departure will be permitted, however, when alternate standards are demonstrated to provide equivalent or better design criteria than the standards in these sections. Conversely, compliance is required with State and local codes where such requirements provide a standard higher than those in these sections. The additional cost, if any, in using standards that are higher than those of VA should be documented and justified in the application.

(d) The space criteria and area requirements referred to in these standards shall be used as a guide in planning. Additional area and facilities beyond those specified as basic may be included if found to be necessary to meet the functional requirements of the project but are subject to approval by VA. Substantial deviation from the space or area standards shall be carefully considered and justified. Failing to meet the standards or exceeding them by more than 10 percent in the completed plan would be regarded as evidence of inferior design or as exceeding the boundaries of professional requirements. In those projects that unjustifiably exceed maximum space or area criteria, VA funding may be subject to proportionate reduction in proportion to the amount by which the space or area of the cemetery exceeds the maximum specified in these standards.  (Authority: 38 U.S.C. 501, 2408.)