| Release: Baseline | Test Case Creation Engineer: Will Leverenz |
| --- | --- |
| Title: D2D_Loc_RADAR Test | Date Test Case Created: 03/02/2006 |
| Test Case Execution Engineer: | Pass/Fail/Pending: |
| Test Platform: TBW3 (WFO), TBW4, TBDR, TBDW (SIT) | Total Test Time: |
| Start Date: | Run Time for processes or reports: |
| Complete Date: | Database Instance and Version: PostGres 7.4.8 |
| Logged in User’s Role: | Test Case Version Number: V3 |
| Notification Server Version: OB8.1 | Test Case Version Number Update Date: |
| Last Modified By: Jim Richardson | Location of Test Artifacts for this test case: N/A |
| CI: RD |  |

## Test Case #: D2D_Loc_RADAR_1.4.1.18

### Test Case Description

This test case demonstrates the capability of AWIPS to display different types of local dedicated radar data. In addition, verify that the environmental parameters from the RUC are sent to an ORPG Build 9 radar.

- Requirements

Not Applicable.

- Data Input:

Not Applicable.

- Prerequisite Conditions:

For testing environmental parameters, the testbed must be able to send to an ORPG Build 9 radar.  Currently, TBW3 is set up to send RUC environmental data to KCRI.  The RUC domain has been expanded on TBW3 temporarily so its domain includes KCRI.  When the testbed radars are upgraded to Build 9, the tester may use additional testbeds.

| Step # | Action / Inputs | Expected Outputs | Pass(P)/ Fail(F) Pending (Pen) | DR #, Name, Description for failed step | Special Needs / Comments |
| --- | --- | --- | --- | --- | --- |
|  | Log into an lx workstation. | A terminal window opens and user is able to log in with a password. |  |  |  |
|  | Left click on the desk top and select Start D2D from the list. | The D2D system launches |  |  |  |
|  | From the Scale pull-down menu (left side of toolbar), select WFO. | Main pane map scale changes to selected scale. |  |  |  |
|  | Use the kxxx & txxx menus (local dedicated radars) in D2D to load local radar data. - Select one product at a time. - Do not make an OTR or RMR. - Do not use the RADAR menu. | Products load in main pane. List the dedicated radars displayed: _________________________ _________________________ _________________________ _________________________ |  |  |  |
|  | Select products that display a current time on the drop-down menu. | Compare with time stamps of frames at lower right of screen when display comes up. |  |  |  |
|  | Once the product loads, click on the [>] button to make the product cycle through a full set of frames. | Product has multiple frames available to view (the number selected in the Frames menu option). |  |  |  |
|  | Select Clear on the D2D toolbar menu. | Product is cleared from the main pane leaving only the default map. |  |  |  |
|  | Repeat steps 4-7 until many products have been loaded. For this section, load each product one by one. | Samples of the available products were loaded individually. |  |  |  |
|  | In the D2D menu bar, select txxx > Graphics > VAD Wind Profile Display (VWP) | The main pane will display a two dimensional chart (time vs. height) that will show wind barbs. |  |  |  |
|  | View radar text products: Launch the Text Window by selecting the following from the D2D menu bar: Tools > Text Window | The Text Window opens. |  |  |  |
|  | In the AFOS Cmd text box enter WSRVWPxxx, where xxx is the TDWR radar ID (BWI, JFK, etc.). Press the enter key. | The product loads in the Text Window. |  |  |  |
|  | View sounding radar products: Launch the Volume Browser by selecting the following from the D2D menu bar: Volume > Browser | The Volume Browser opens. |  |  |  |
|  | Select a source: Other > VWP | Source shows up highlighted (yellow) in the source selection list. |  |  |  |
|  | Select Plan View > Sounding then Thermo > Sounding and select an item. | Field shows up highlighted (yellow) in the field selection list. |  |  |  |
|  | Select a plane, for example: Points > Sounding A Make sure the point selected is near a TDWR radar. | Plane shows up highlighted (yellow) in the plane selection list; product shows up highlighted in the product selection list. |  |  |  |
|  | Open a terminal window and log into dx2f by typing: ssh dx2f | User is logged into dx#-<site1> (where # = 2, or 1 if there is a failover.) |  |  |  |
|  | Confirm sending RUC environmental parameters to an ORPG Build 9 radar: On dx2f, verify that at the top of each hour sendEnvironData.csh is scheduled to execute by typing: grep sendEnv /etc/cron.d/* | The sendEnvironmentalData log files are created at the top of the hour using a cron job: 0 * * * * fxa csh –c ‘${FXA_HOME} /bin/sendEnvironData.csh >& /dev/null’ |  |  |  |
|  | A log file is created each time the process is executed. Verify a log file is created for each hour by typing: logs ll sendEnvironmentalData* | The sendEnvironmentalData log files show the data are successfully written and transferred to the specified ORPG. |  |  |  |
|  | Check information about the environmental data that is being sent by typing: grep EVENT sendEnv* or more sendEnv* or grep -in “ K” sendEnv* If the testbed does not have ORPG Build 9 (it should be in OB8.1), skip to step 23. | A typical log file will include some of the following: radarName (with lat/lon) percentage inventory for each parameter (GH, RH, T, uW, vW, Px SFC) the levels for each parameter sent model data info date/time info forecast hour (forecast_hr) coordinate system (coord_system) projection (proj) lats/longs data successfully compressed (compressed and uncompressed length) data are successfully written to $FXA_DATA/radar/environData connection successful to RadarServer completion of sending data to the local ORPG |  |  |  |
|  | On dx2, verify that the ORGP CommsMgr is running by typing: ps –ef ¦ grep ORPG If the ORPGCommsMgr is not running, start it by typing: /awips/fxa/bin/ORPGCommsMgr <kxxx> | ORPGCommsMgr is up and running. Note: substitute the name of a kxxx or txxx radar from the menu bar for <kxxx>. |  |  |  |
|  | After the top of the hour, verify notification in the RadarServer logfile by typing: tail –f sendEnvironmentalData* | In the RadarServer log, receipt messages are found like: ENV_DATA message received to be sent to RPG 347: type 5 Sending env data 5 to KCRI |  |  |  |
|  | In the ORPGCommsMgr log, look for notification log messages by typing: ls –ltr ORPGC* grep –C 5 ENV_ ORPGC* ¦ more | In the ORPGCommsMgr log, verify there are receipt messages, similar to these: radar id = 347 ENV_DATA message received to be sent to RPG 347: type 5 orpg Normal channel: nn bytes written deket[]ing msg nn bytes are successfully sent to RPG. File /data/fxa/radar/environData/<yy yymmdd_hhmmss>.kcri is deleted. |  |  |  |
|  | Verify that the ORPGCommsMgr deletes the compressed files in /data/fxa/radar/environData by typing: ls –l /data/fxa/radar/environDa ta/*<kxxx> | The compressed file named just above has been removed from /data/fxa/radar/environData. Note: insert the name of a radar from the menu bar for <kxxx>. |  |  |  |
|  | Close the terminal window by typing: Exit | The window closes. |  |  |  |
|  | Close D2D by clicking on File ¦ Exit | The application closes and this test case is completed. |  |  |  |