ViTS Roll-About User Guide (Polycom ViewStation FX)

January 2006

NASA Integrated Services Network

Contents

1.	Purpose	1

2.	Scope	1

3.	Remote Control	1

4.	Video Plasma Screen	2

5.	Network Connectivity	3

5.1	Network Line Check	3

5.2	Placing a Video Call	4

5.3	Point-to-Point Call Procedure	4

5.4	Multi-point Call Procedure	7

5.5	Multi-point Dialing Speed Information	7

5.6	Multi-point Viewing Modes	8

5.6.1	Automatic, Discussion, Presentation, and Full Screen modes	8

5.6.2	Auto	8

5.6.3	Discussion	9

5.6.4	Presentation	9

5.6.5	Full Screen	9

5.7	Mode Switching	9

5.8	Adding a Telephone Call to a Video Call	9

5.9	Answering a Video Call	10

5.10	Placing an Audio Only Conference Call	10

5.11	Address Book/Speed Dial	11

5.11.1	Adding an Entry to the Address Book	12

5.11.2	Editing an Existing Entry in the Address Book	12

5.11.3	Deleting Entries in the Address Book	13

5.12	Cameras	13

5.12.1	Camera Settings	13

5.12.2	Camera Adjustment	13

5.12.3	Adjusting a Second Camera (optional feature)	14

5.12.4	Automatic Voice Tracking	14

5.12.5	Automatic Tracking of Camera Presets	14

5.12.6	Assigning Camera Preset Positions	15

5.13	Sound Control	15

5.14	Audio/Video Source Control	16

5.14.1	Selecting A Near-Site Video Source	16

5.15	Selecting a Far-Site Video Source	17

5.16	Optional Equipment	17

5.16.1	Video Cassette Recorder (VCR)	17

5.16.2	Document Camera	17

6.	Change Log	18

Appendix A. Abbreviations and Acronyms	19

ViTS Roll-About User Guide

(Polycom ViewStation FX)

# Purpose

The purpose of this guide is to familiarize the user with the functions and use of the Roll-About Video Teleconferencing System (ViTS).

# Scope

The Video Roll-about (VRA) is a roll-about videoconference system designed for smaller conference rooms and office areas and can be relocated easily to different rooms that contain network drops.  VRA systems support data rates ranging from 128 Kilobits per second (kbps) to 1472 kbps.  The VRA contains an on-board Multipoint Control Unit (MCU) capable of supporting up to three additional video sites, depending on network bandwidth allocation.  It also provides audio add-on capability for interactive conferencing with voice systems.

The VRA consists of a Polycom ViewStation FX control system that is controlled by a user friendly, handheld remote control, and features a 50" plasma screen mounted on a roll-about cart.  Optional equipment includes a Video Cassette Recorder (VCR) and document camera with stand.

The ViewStation FX may be substituted with an MP-512 model.  It is a less expensive system that is limited to a data rate of 512 kbps.  It consists of the same operational features as the ViewStation FX.

# Remote Control

The remote control is an integral part of the system.  You can use the remote control to configure and operate the ViewStation FX.  Once you have the system set up and running, press the yellow INFO button on the remote control for a basic description of the remote control button.

# Video Plasma Screen

The 50” video plasma screen is operated by a handheld remote control.  There are four types of viewing modes:  zoom, normal, full, and stadium.  Stadium is the recommended viewing mode.  To change viewing mode on the plasma screen, press the WIDE button until the desired viewing mode is on the screen.  Plasma screen audio can be adjusted using the volume up and down buttons on the remote control, and should stay at one-half its maximum volume.

# Network Connectivity

## Network Line Check

Each time the ViewStation FX is powered up, a numbered yellow icon appears for every network line below the Video Call icon.  This yellow icon indicates that the ViewStation FX is checking to see if the network lines are connected.  If the icon changes to a green up arrow, the ViewStation FX has found the network line.  If the icon changes to a red down arrow, the ViewStation FX was unable to find the network line. In this case, check your network connection and verify that you entered the numbers correctly.

## Placing a Video Call

The following procedures are the manual instructions for placing video calls to other units.  If only two video sites are connected, it is referred to as a “Point-to-Point” call.

If more than two locations will be connected in a videoconference, it is referred to as a

“Multi-Point” call.

Video calls may also be placed using the Address Book/Speed Dial feature (see section titled Address Book for more information).

## Point-to-Point Call Procedure

Using the NEC Plasma Remote Control (RP-100), turn the plasma video screen power “ON”, then press the “WIDE” button to select the desired viewing mode (Stadium is the recommended choice).

Then, using the Polycom Handheld Remote Control unit, perform the following:

- Press the MENU button to bring up the Polycom main menu page.

- Use the arrow buttons on the remote control to highlight the Video Call icon and press the SELECT button (the round button in the center of the arrow keys).  The following screen will appear:

- Use the arrow buttons on the remote control to highlight the Speed icon on the screen and then select the proper speed for the video connection from the drop-down menu.

*Note: For 2x56 or 2x64 videoconferences, the speed must be selected prior to typing in the video dial numbers in order for two text fields to appear (one for each video dial number).

- Use the numeric keypad on the remote control to enter the video dial number(s) into the text field(s) at the top of the screen.  If alpha characters are required, press the AUTO button on the remote control to bring up the keyboard (If an error is made, use the arrow keys to undo the wrong number(s) and re-enter the proper ones or use the arrow keys to highlight the Clear field, and press the SELECT button to clear all data).

- Press the green CALL•HANG-UP button on the remote control to place the video call.  The number and the speed of the site you are dialing appear at the top of the screen.  The call progress indicators on the lower left side of the screen indicate that the call is being established.  They change progressively to blue, yellow, orange, and green as your call completes.

- When the call completes, the party called appears on the screen, and your site will appear in the picture-in-picture (PIP) window at the lower right.  If you have two video monitors, the party dialed will appear on the main monitor, and you will appear on the second monitor.  If the call does not complete, an error message is displayed.  If an error message is received, press the INFO button on the remote control for an explanation.

- To end the video call, press the CALL•HANG-UP button on the remote control.  The following screen appears.

- Highlight the Disconnect Video Call icon and press the SELECT button on the remote control.  If the call was made with a number that is not in your Address Book, a dialog box gives you the opportunity to add the number.  If Yes is selected, the system takes you to the address book where you can save the information.  If No is selected, the main screen appears on the monitor.

*Note:  If you remain on this screen for 60 seconds without selecting Stay In Call or Disconnect Video Call, the call is automatically disconnected.

Be sure to turn power “OFF” to the NEC Plasma Video Screen!

(Not turning off the unit will cause damage to the screen)

## Multi-point Call Procedure

The ViewStation FX contains an on-board Multipoint Control Unit (MCU) capable of supporting up to three additional video sites, depending on network bandwidth allocation.  If more than four sites are needed in a multipoint conference, it should be scheduled using the National Aeronautics and Space Administration (NASA) Integrated Services Network (NISN) Bridging Service (see procedure located at http://www.nisn.nasa.gov/vits/wcmultisched.doc).

To establish a Multi-point Videoconference using the ViewStation FX MCU, perform the following:

- Place a video call to the first site (see Point-to-Point Call Procedure).

- Press the CALL•HANG-UP button on the remote control. The Call Hang-up Choices screen appears.

- Highlight the Add a Video Call icon and press the SELECT button on the remote control.  The Video Phone screen appears.

- Use the keypad to enter the video dial number(s) into the text field at the top of the screen or use Speed Dial in the Address Book. Press the CALL•HANG-UP button on the remote control to place the call.  The video call connects.

- Repeat steps 2 through 4 until all of the sites are connected.

*Note: While dialing each additional site, a split-screen effect will show all sites that are connected in the video call.

## Multi-point Dialing Speed Information

If circuit bandwidth allows, up to four locations may participate in a video call with the ViewStation FX.  The following chart shows the maximum allowable dialing speeds according to the number of sites in a call.

## Multi-point Viewing Modes

There are four different viewing modes available in a Multi-point call:

### Automatic, Discussion, Presentation, and Full Screen modes

The default mode is Auto, which switches between Discussion and Presentation modes automatically, depending on the conversational style of your meeting.

### Auto

In Auto Mode, the system determines the optimal viewing mode based on the interaction between the sites. If more than one site is talking at the same time, the system uses Discussion mode.  If one site is talking uninterrupted, the system uses Presentation mode. The system takes about 15 seconds to decide whether there is a single presenter before switching to Presentation Mode. If one of the far sites interrupts the presenter for several seconds during Presentation mode, the system immediately switches to Discussion mode.

### Discussion

In Discussion Mode, all of the sites can see everyone in the meeting at the same time. This feature is sometimes referred to as Continuous Presence Mode. You see yourself as one of the sites. Your picture might be slightly delayed if you are in a Multi-point call. This is normal. The far sites hear your voice synchronized with your motion.  If you are using a single-monitor system, sites appear on screen in as many windows as there are sites in the call. If you are using a dual-monitor system in a four-way call, the near site (you) appears in the second television monitor and the far sites appear in windows on the first television monitor. If you are using a dual-monitor system in a three-way call, each far site appears full screen on each monitor and the near site appear in PIP window on the main monitor.

### Presentation

In Presentation Mode (also called voice-activated switching), the person who is speaking appears full screen to the far sites. If you are using a single-monitor system, the speaker or presenter appears full screen on your monitor.  Your picture automatically appears in a PIP window when you raise your remote control. If you are using a dual-monitor system, the person speaking appears in the main monitor, and the other parties appear in windows on the second monitor.

### Full Screen

In Full Screen Mode, every site in the call sees the speaker full screen.

## Mode Switching

To switch Multi-point meeting modes, perform the following:

- From the main calling screen, select System Info>User Setup.

*Note:  If you are switching modes during a Multi-point call, press the MENU button on the remote control to go to the main calling screen.

- Select the MP Mode field.  The Multi-Point Setup screen appears.

- Select Auto, Discussion, Presentation, or Full Screen mode.

# Press the MENU button on the remote control until you return to the main screen.

## Adding a Telephone Call to a Video Call

In countries where it is approved, an analog telephone line can be connected to the ViewStation FX.  This makes the ViewStation FX capable of allowing telephone call participants to be added to a video call.

After the video call is established, a telephone call may be added as follows:

- Press the CALL•HANG-UP button on the remote control. The Call Hang-up Choices screen appears.

- Select the Add Speakerphone icon and press the SELECT button.  The Telephone screen appears.

- Enter the phone number of the audio-only party using the numeric keypad on the remote control and press the SELECT button.  The ViewStation FX begins dialing the audio-only party.

- After the audio-only party connects, press the NEAR or FAR button on the remote control to return to the videoconference.

*Note: Three-way calling is only supported if you have enabled three-way calling from your local telephone company.  Select “Flash, #, 1” on the telephone screen to obtain another line (See “Placing an Audio-Only Conference Call” for detailed three-way calling procedure).

- To disconnect the telephone call, press the CALL•HANG-UP button on the remote control. The Call Hang-up Choices screen appears.

- Select the Disconnect Speakerphone Call icon and press the SELECT button.  The audio-only party disconnects.

## Answering a Video Call

The ViewStation FX is set by default to automatically answer incoming calls.  This option can be disabled in the General Setup screen by selecting System Info>Admin Setup>General Setup.

To answer an incoming video call manually, highlight Yes when the ViewStation FX prompts you, and press the SELECT button on the remote control.

## Placing an Audio Only Conference Call

In countries where it is approved, an analog telephone line can be connected to the ViewStation FX.  This makes the ViewStation FX capable of being used as a standard speakerphone, allowing telephone calls and three/four-way conferences to be established.

Complete the following steps to place a telephone call from your ViewStation FX:

- From the main calling screen, select Telephone and press the SELECT button.  The Telephone screen appears.

- Use the numeric keypad on the remote control to enter the number you want to dial.  If you are dialing within your Private Branch Exchange (PBX) system, you only have to dial the last four digits of the number.  If you want to delete a digit, press the LEFT ARROW button on the remote control.  To delete an entire phone number, highlight the Clear icon on the screen and press the button.

- Press the CALL•HANG-UP button on the remote control to place the call.

Note: Three-way calling is only supported if you have enabled three-way calling from your local telephone company.  Select “Flash, #, 1” on the telephone screen to obtain another line. (See “Placing an Audio-Only Conference Call” section for detailed three-way calling procedure).

# To end the call, press the CALL•HANG-UP button on the remote control.

## Address Book/Speed Dial

The Address Book saves time by allowing you to place video calls by name. You can pre-program up to 1,000 entries in the Address Book.

To access the Address Book:

- Select the Address Book icon on the main screen.  The Speed Dial screen appears.

- Highlight the Address Book icon again and press the SELECT button on the remote control. The main Address Book screen appears as follows.

### Adding an Entry to the Address Book

An entry can be added to the Address Book as follows:

- Highlight the New icon and press the SELECT button on the remote control.  The following screen appears:

- Highlight the One Site icon and press the SELECT button on the remote control.  The Add/Change Entry screen appears.

- Use the on-screen keyboard and the remote control to enter the necessary information on this screen.  To enter a dot, press the RIGHT ARROW button on the remote control.

4. Highlight the Save icon and press the button on the remote control.  You then return to the main Address Book screen.

### Editing an Existing Entry in the Address Book

An existing Address Book entry may be edited as follows:

- Use the UP and DOWN arrow buttons on the remote control to highlight an Address Book entry.

- Highlight the Edit icon and press the SELECT button on the remote control.  The Add/Change Entry screen and the on-screen keyboard appear.

- Use the on-screen keyboard and the remote control to change the information on this screen as needed.  In the name field, use the backspace key on the on-screen keyboard to delete letters.  In the number field, use the LEFT ARROW button to delete numbers.

# Highlight the Save icon and press the SELECT button on the remote control.  Your changes are saved and you return to the main Address Book screen.

### Deleting Entries in the Address Book

An existing entry in the Address Book may be deleted as follows:

- Highlight the entry you want to delete.

- Use the left arrow button to highlight the Delete icon.

- Press the SELECT button on the remote control.  The entry you selected is now deleted from the Address Book.

## Cameras

### Camera Settings

The settings of the cameras can be adjusted from the Cameras screen.  To access this screen, select System Info>Admin Setup>Video/Camera>Cameras.

*Note:  Other sites can control the camera in your room during a video call if the Far Control of Near Camera option is enabled within your ViewStation FX Camera settings.  The camera may be adjusted at the far site in a call if that site has its Far Control of Near Camera option enabled.

### Camera Adjustment

While in a video call, if you have to go to any of the ViewStation FX menu screens, pressing the NEAR or FAR button on the remote control will return you to the normal video call view.

To control or adjust the camera on your ViewStation FX, press the NEAR button on the remote control.  Your camera view appears full screen on the video monitor.  A camera icon appears in the upper right corner pointing toward you.

If the Far Control of Near Camera option is enabled on the far-site ViewStation FX, you can control or adjust the camera at the far site by pressing the FAR button on the remote control. The far site camera’s view appears full screen on the television monitor. A Camera icon appears in the upper right corner pointing away from you. Use the remote control to adjust the far-site camera the same way you would adjust your camera.

Tilt, Pan—Use the arrow buttons on the remote control to tilt the camera up and down and to pan from side to side.

Zoom—Use the ZOOM buttons to zoom in and out.

The following picture shows the buttons that are used on the remote control to control the camera.

### Adjusting a Second Camera (optional feature)

If an additional camera is connected to your ViewStation FX, you can also adjust the pan/tilt/zoom with the remote control.

To adjust the second camera, press the NEAR button twice. Icons appear for all of the connected local cameras.  Use the arrow keys to select the icon for the second camera and press the enter button on the remote control.  (See detailed instructions in “Camera Adjustment” section to make camera adjustments.)

### Automatic Voice Tracking

The main camera on your ViewStation FX can automatically move to whoever is speaking in the meeting.  The first time it moves to a person, it might take several seconds of continuous speech to locate the person speaking.  It picks out the position quickly the next time the person speaks.  To enable automatic voice tracking, press the AUTO button once on the remote control.  A Camera icon with a motor attached appears in the upper right corner of the main monitor.  To turn off automatic voice tracking, pan, tilt, or zoom the camera.  Any of these actions returns the camera to manual mode.

### Automatic Tracking of Camera Presets

The ViewStation FX main camera can automatically track to preset positions, giving you greater flexibility and control of automatic voice tracking.  To enable automatic tracking of camera presets, perform the following:

- Select the far or near camera and press the AUTO button twice to enable automatic tracking to preset positions.

- The camera moves to the preset nearest to the person speaking.  You can disable automatic tracking of camera presets by moving the selected camera with the ARROW buttons on the remote control.  Automatic camera tracking is temporarily disabled under the following conditions:

- When your site is on MUTE.

- When there are loud noises coming from the far site or when the far site is speaking.

- When the near site moves the camera.  (Any pan, tilt, or zoom done with the remote control returns the camera to manual mode.)

### Assigning Camera Preset Positions

The system will store up to ten preset camera positions. These ten camera presets can be distributed between the far camera and up to four near-site cameras.  Complete the following steps to program each camera preset button:

- Press the NEAR or FAR button on the remote control to select the near or far camera.

- If you pressed the NEAR button, press it again to select the near-site camera.

- Position the camera using the arrow buttons and ZOOM buttons on the remote control.

- Press the enter button on the remote control. The camera preset circles are now displayed.  A “Press 0-9 to store a preset” message appears on the main monitor.

Note 1:  If the circle is transparent, the preset is empty.

Note 2:  If the circle is solid yellow, the preset is assigned.

Note 3:  To clear all the presets, press the pound (#) key on the remote control.

- Enter a circle number on the remote control keypad to save the current camera position to the selected preset button.

- To view any of the camera preset positions, press the NEAR or FAR button and use the keypad to select the number of the camera preset position to be viewed.

## Sound Control

The volume on the ViewStation FX is related to the volume on the television monitor and can be adjusted by performing the following:

- Set the volume on the television monitor to one-half its maximum volume.

- To adjust the volume on the ViewStation FX, press the VOLUME buttons on the remote control.

MUTE Button and Indicator – To prevent far-site participants from hearing your conversation, press the MUTE button on the remote control or on the microphone pod. Notice that the red light on top of the microphone pod is illuminated.  The Mute icon appears in the bottom left corner of the television monitor indicating to the near and far sites that mute is turned on.  This mute indicator feature is supported in ISDN and H.323 calls.  However, the mute indicator for H.323 calls is only supported by Polycom endpoints.

Note:  There is also an internal volume setting within the Setup menus of the ViewStation FX:

- To adjust this volume setting, select System Info>Admin Setup>Phone/Audio.

- Select the Sound Effects Volume field.

- Adjust the system volume setting by using the volume control buttons on the remote control.

## Audio/Video Source Control

### Selecting A Near-Site Video Source

To select a near-site camera or video source, perform the following:

- Press the NEAR button twice on the remote control and a Camera icon pointing toward you appears.  Numbered local video sources will also appear at the bottom of the screen.

1 = main camera

2 = document camera

3 = VCR

4 = 2nd pan/tilt/zoom camera

- Use the LEFT or RIGHT arrow keys on the remote control to highlight a camera or video source.  Then press the SELECT button on the remote control –or- after pressing the NEAR button once on the remote control, press button 1, 2, 3, or 4 to choose a specific video source.

Note: Make sure that the video source icons are displayed on screen.  Otherwise, when the number button is pressed, a camera preset will be selected instead of a different video source.

- The ViewStation FX displays a full screen view of the current video source on the television monitor.  A Camera icon appears in the upper right corner pointing toward you.

## Selecting a Far-Site Video Source

- To select a far-site camera or video source during a videoconference, press the FAR button twice on the remote control. A Camera icon pointing away from you (toward the far site) appears.

- Press the LEFT or RIGHT arrow key on the remote control to highlight a video source.  Then press the SELECT button on the remote control.

-or-

Press the FAR button twice, then press button 1, 2, 3, 4, or 5 to choose a specific camera.

- Press the SELECT button on the remote control.

- The ViewStation FX displays a full screen view of the far-site camera’s current video source on the television monitor.

Note:  If there is no camera or other input equipment connected to the selected video source, you will see either a blue screen or frozen video from the last video source.

## Optional Equipment

### VCR

A VCR can be used to record your videoconference or to present recorded material as part of your videoconference.  The VCR records video from the near site’s main television monitor and audio from both the near and far sites.  When playing tapes, the VCR transmits audio and video to all participants in a call.

- To play a tape in the VCR, press the NEAR button on the remote control once.

- Use the ARROW buttons to highlight the VCR icon on the screen. Press the SELECT button on the remote control.

- Use the VCR remote control to play the tape.

### Document Camera

A document camera can be used to take pictures (snapshots) of an object or document and send them to a far site.  The image being displayed on the document camera surface may also be transmitted as a full-motion video source.

To send the document camera as a full-motion source, use the ViewStation FX remote control and perform the following:

- Press the NEAR button once to bring up the video source icons at the bottom of the screen.

- Then use the ARROW buttons to highlight the Document Camera icon on the screen.

- Press the SELECT button on the remote control.

To send a snapshot, use the ViewStation FX remote control and perform the following:

- Press the “SNAPSHOT” button twice.  The snapshot appears on the video monitor.

2.	To return to camera view, press the NEAR button.

For a complete USER MANUAL connect to:

http://www.polycom.com/common/pw_item_show_doc/0,1449,981,00.pdf

# Change Log

| Status (Baseline/Revision/ Cancelled) | Document Revision | Effective Date | Revision Purpose |
| --- | --- | --- | --- |
| Baseline | 0 |  | UNITeS original issuance |

Abbreviations and Acronyms

| Acronym | Definition |
| --- | --- |
| ISDN | Integrated Services Digital Network |
| Kbps | Kilobits per second |
| MCU | Multi-point Control Unit |
| NASA | National Aeronautics and Space Administration |
| PBX | Private Branch Exchange |
| PIP | Picture-in-Picture |
| VCR | Video Cassette Recorder |
| ViTS | Video Teleconferencing System |
| VRA | Video Roll-About |

# Text boxes

#### Far