# CDF Silicon Vertex Detector Low Voltage Power Pigtail Cable: Safety Information for the CDF Cable Committee	3/6/2000

The document gives the specifications and safety information for the CDF Silicon Vertex Detector low voltage power pigtail cable that runs from the junction cards to the SVXII port cards.

Direct questions and comments to:

Matthew Herndon    Phone: (630) 840-8619

(Physicist)                Fax:     (630) 840-6315

Email:  herndon@fnal.gov

Low Voltage Power Cable

##### Cable

#### Description

Overview: Custom 24 multi-conductor round cable with different gauge sizes depending on the channel

Belden MIL-W-16878/1-PVC 8500 series type 8502-8505, stranded copper PVC cable

8502 20 AWG AVDD Layer 4

8503 22 AWG DOIMs and AVDD Layers 2 and 3

8504 24 AWG AVDD Layer 1

8505 26 AWG DVDDs and AVDD Layer 0

Jacketed with

Alpha GRP-120NFNF12, Non-fraying, expandable braided polyester sleeving

#### Note conductors will be color coded

#### Manufacturer: Belden and Alpha

#### Cable Type: Round custom cable

#### Part Number: Belden MIL-W-16878/1-PVC 8500 series type 8502-8505 and Alpha GRP-120NFNF12

#### Function: Supplies low voltages to the SVXII port card and the SVX3 IC.

#### Length: 6ft

#### Location_1: Just inside ISL space frame

#### Location_2: Just outside SVXII barrels

#### Fire Safety

#### Flame test rating: Cables Rated for 105 C @ 600V

#### Jacketing  Rated for 125 C

#### Both: UL VW-1

#### Insulation material: PVC

#### Jacket material: Polyester

#### Electrical Considerations

#### Power conductor ampacity: 2.8 Amp In addition highest current line has been reduced by a factor of 2 by using two conductors.

#### Power conductor over-current protection: Fused at power supply.  Also hardware and software trip control. As the maximum current for any supply is below the rated maximum of the cable assembly, fusing of individual lines is not necessary.

#### Connectors

24 pin Micro-Fit wire-mount circuit receptacle

Part #: Molex 43025-2400

http://www-cdf.fnal.gov/upgrades/svxii/barrel_testing/molex_43025-2400.ps

Receptacle pins

Part #: Molex 43030-0002 and 43030-0005 as appropriate

http://www-cdf.fnal.gov/upgrades/svxii/barrel_testing/molex_43030-0002.ps

(Note mating connector Part #: Molex 43045-2418

http://www-cdf.fnal.gov/upgrades/svxii/barrel_testing/molex_43045-2419.ps)

#### Pin out: Labeled by HDI(1-5)

| PIN # | Conductor Number | Description | Comment: Color when using Beldon single wire cable | Color when using spectra-strip 22 and 26 AWG ribbon cable |
| --- | --- | --- | --- | --- |
| 1 | 1 | +5V DOIM | AWG 22 color 17 white/yellow | Black |
| 13 | 2 | +5V DOIM | AWG 22 color 18 white/blue | White |
| 2 | 3 | DG DOIM | AWG 22 color 19 white/brown | Grey |
| 14 | 4 | +2V DOIM | AWG 22 color 20 white/orange | Violet |
| 3 | 5 | DG 1 | AWG 26 color 1brown | Brown |
| 15 | 6 | DVDD 1 | AWG 26 color 2 red | Red |
| 4 | 7 | DG 2 | AWG 26 color 3 orange | Orange |
| 16 | 8 | DVDD 2 | AWG 26 color 4 yellow | Yellow |
| 5 | 9 | DG 3 | AWG 26 color 5 green | Green |
| 17 | 10 | DVDD 3 | AWG 26 color 6 light blue | Blue |
| 6 | 11 | DG 4 | AWG 26 color 7 violet | Violet |
| 18 | 12 | DVDD 4 | AWG 26 color 8 gray | Grey |
| 7 | 13 | DG 5 | AWG 26 color 9 white | White |
| 19 | 14 | DVDD 5 | AWG 26 color 10 black | Black |
| 8 | 15 | AG 1 | AWG 20 color 4 yellow (layer 4) |  |
| 20 | 16 | AVDD 1 | AWG 20 color 5 green |  |
| 9 | 17 | AG 2 | AWG 24 color 14 white/black (layer 1) |  |
| 21 | 18 | AVDD 2 | AWG 24 color 16 white/green |  |
| 10 | 19 | AG 3 | AWG 26 color 17?? White/yellow (layer 0) | Brown |
| 22 | 20 | AVDD 3 | AWG 26 color 22 white/violet | Red |
| 11 | 21 | AG 4 | AWG 22 color 21 white/gray (layer 3) | Blue |
| 23 | 22 | AVDD 4 | AWG 22 color 1 brown | Green |
| 12 | 23 | AG 5 | AWG 22 color 2 red (layer 2) | Yellow |
| 24 | 24 | AVDD 5 | AWG 22 color 3 orange | Orange |

#### Maximum voltage and current per supply

| Supply Name | Maximum Voltage(V) | Maximum Current(A) | AWG |
| --- | --- | --- | --- |
| AVDD 0 | 10.0 | 0.6 | 26 |
| AG 0 | 0.0 | 0.6 | 26 |
| AVDD 1 | 10.0 | 0.9 | 24 |
| AG 1 | 0.0 | 0.9 | 24 |
| AVDD 2 | 10.0 | 1.5 | 22 |
| AG 2 | 0.0 | 1.5 | 22 |
| AVDD 3 | 10.0 | 1.5 | 22 |
| AG 3 | 0.0 | 1.5 | 22 |
| AVDD 4 | 10.0 | 2.1 | 20 |
| AG 4 | 0.0 | 2.1 | 20 |
| DVDD 0 | 8.0 | 0.6 | 26 |
| DG 0 | 0.0 | 0.6 | 26 |
| DVDD 1 | 8.0 | 0.9 | 26 |
| DG 1 | 0.0 | 0.9 | 26 |
| DVDD 2 | 8.0 | 1.5 | 26 |
| DG 2 | 0.0 | 1.5 | 26 |
| DVDD 3 | 8.0 | 1.5 | 26 |
| DG 3 | 0.0 | 1.5 | 26 |
| DVDD 4 | 8.0 | 2.0 | 26 |
| DG 4 | 0.0 | 2.0 | 26 |
| +5V DOIM | 8.0 | 2.8, 1.4 per line | 22, two lines |
| +2V DOIM | 3.5 | 1.7 | 22 |
| DG DOIM | 0.0 | 1.1 | 22 |