(WQ – 5) Water Quality Infiltration Assessment Guide

| ECiw (dS/m) | SAR | * adj.RNa |  | Infiltration Assessment (Affects infiltration rate of water into the soil. Evaluated using ECiw & SAR or adj.RNa together) |
| --- | --- | --- | --- | --- |
|  | High Ca Low Na | High Na Low Ca | High Ca Low Na Low HCO3 | High Ca Low Na High HCO3 | High Na Low Ca Low HCO3 | High Na Low Ca High HCO3 |  |  |
|  |  |  |  |  |  |  |  | SAR Or adj.RNa | Degree of Restriction on USE ECiw (dS/m) |
| 0.5 | 0.71 | 4.0 | 0.64 | 0.9 | 3.2 | 4.3 |  |  | None | Slight to Moderate | Severe |
| 1.0 | 1.0 | 5.7 | 1.2 | 1.6 | 5.7 | 7.2 |  | 0 – 3 | >0.7 | 0.7 - 0.2 | <0.2 |
| 2.0 | 1.41 | 8.1 | 2.1 | 2.8 | 9.7 | 11.5 |  | 3 – 6 | >1.2 | 1.2 – 0.3 | <0.3 |
| 3.0 | 1.73 | 9.9 | 3.0 | 3.7 | 13.1 | 14.8 |  | 6 – 12 | >1.9 | 1.9 – 0.5 | <0.5 |
| 4.0 | 2.0 | 11.4 | 3.7 | 4.5 | 15.6 | 17.6 |  | 12 – 20 | >2.9 | 2.9 – 1.3 | <1.3 |
| ECiw =Electrical Conductivity of irrigation water; SAR = Sodium Adsorption Ratio; adj.RNa = adjusted Residual Sodium (the adj.RNa replaces the older adj.SAR method which is no longer recommended) |  | 20 - 40 | >5.0 | 5.0 – 2.9 | <2.9 |
| Potential Reduction in Infiltration due to SAR (or adj.RNa) and ECiw (Soil Type determines degree of problem) |  | NOTE: the SAR and adj.RNa calculations were based on the following concentrations: High Ca = 70% of meq./l of cations Low Na = 20% of meq./l of cations Low HCO3 = 20% of meq./l of anions Low Ca = 20% of meq./l of cations High Na = 70% of meq./l of cations High HCO3 = 70% of meq./l of anions Magnesium was kept at 10% of meq./l of cations Rudy Garcia 2008 |
| Least affected-------- -------Moderately affected-------- ------Most affected |  |  |
| Coarse | Moderately Coarse | Medium | Moderately Fine | Fine |  |  |
| Sands, fine Sands, V. fine Sands, Loamy Sands, Loamy F. Sands, LoamyV. F. Sand | Sandy Loam, fine Sandy Loam | Very fine Sandy Loam, Loam, Silt Loam, Silt | Sandy Clay Loam, Silty Clay Loam, Clay Loam | Sandy Clay, Silty Clay, Clay |  |  |