JRA3 in the CARE proposal

Version 26/09/2003

Title: High Intensity Pulsed Proton Injectors

Acronym: HIPPI	Coordinator: R. Garoby (CERN)

Participating Laboratories and Institutes:

| Institute (participant number) | Acronym | Country | Coordinator | Scientific Contact | Associated to |
| --- | --- | --- | --- | --- | --- |
| CCLRC Rutherford Appleton Laboratory (20) | CCLRC | UK | P. Norton | C. Prior |  |
| Commissariat à l’Energie Atomique (1) | CEA | F | R. Aleksan | A. Mosnier |  |
| CERN (17) | CERN | CH | H. Haseroth | R. Garoby |  |
| Forschungszentrum Jülich (7) | FZJ | D | R. Tölle | R. Tölle |  |
| Gesellschaft für Schwerionenforschung, Darmstadt (4) | GSI | D | N. Angert | L. Groening |  |
| Institut für Angewandte Physik - Frankfurt University (5) | IAP-FU | D | U. Ratzinger | U. Ratzinger |  |
| INFN-Milano (10) | INFN-Mi | I | S. Guiducci | C. Pagani | INFN |
| CNRS Institut de Physique Nucléaire d’Orsay (3) | CNRS-IN2P3-Orsay | F | T. Garvey | T. Junquera | CNRS |
| CNRS Laboratoire de Physique Subatomique et de Cosmologie (3) | CNRS-LPSC | F | T. Garvey | J.M. De Conto | CNRS |

Main Objectives: Research and Development of the technology for high intensity pulsed proton linear accelerators up to an energy of 200 MeV.

Cost:

| Total Expected Budget | Requested EU Funding |
| --- | --- |
| 12 M€ (FC) + 2.7 M€ (AC) Total 14.7 M€ | 3.6 M€ |

# 1. Scientific and Technological excellence

Requests from the various physics communities for secondary particle beams have recently drastically increased. Therefore, a number of European laboratories have pursued separate development programmes concerning the high intensity proton linac that can deliver the primary beam onto the target. In particular:

- CEA and CNRS-IN2P3-Orsay on the low-energy section (3 MeV) (IPHI project),

- Frankfurt University (Germany) on high-efficiency accelerating structures,

- CERN on chopping and medium-energy accelerating structures,

- CCLRC-RAL on the chopper design, ion source and RFQ development,

- INFN-Mi (Italy), CEA (France), FZJ (Germany), CNRS-IN2P3-Orsay and CNRS-LPSC (France) on superconducting accelerating structures.

All these laboratories, together with GSI (Germany), have developed beam dynamics tools aimed at mastering high-intensity beams in linacs.

# Objectives and originality of the joint research activity

    - Objectives

The HIPPI JRA is meant to foster the development of a common European technology base for the construction of high intensity pulsed linear accelerators. It will achieve this by coordinating the above-mentioned efforts, realising a systematic study of several technological alternatives up to an energy of 200 MeV. The proposed R&D activities are intended to surpass the level of competence achieved outside Europe and provide the technological background for substantial improvements of facilities at three European Laboratories:

- CERN :

  - Improve the proton flux for fixed target experiments

  - Upgrade the neutrino beams for CNGS experiment

  - Increase the proton flux for the ISOLDE facility

  - Improve the stability, reliability and integrated luminosity of the LHC

- CCLRC-RAL :

  - Increase the neutron flux of ISIS and the potential for neutrino beams

- GSI :

  - Increase the proton flux of the heavy ion synchrotron (SIS)

Although the detailed specifications will only be defined at the first general meeting, in the autumn of 2004, the basic goals are as follows:

- for normal-conducting accelerating structures: shunt impedance ZT2 (power efficiency) higher than 40 M/m in the energy range 3-100 MeV, at a competitive cost with respect to conventional DTL.

- for superconducting accelerating structures: gradient exceeding 7 MV/m with Q 1010 in the energy range 100-200 MeV, at a construction cost comparable to normal-conducting structures. Development of efficient superconducting structures down to beam energies around 5 MeV

- for beam chopping: switching time smaller than the distance between bunches at 352 MHz (about 2 ns). Moreover, the overall design of the chopper-line has to minimize emittance growth.

- for beam dynamics: experimental validation of simulation codes, and rules for a design keeping the uncontrolled beam loss below 1W/m (threshold for hands-on maintenance) all along a high energy linac (> 1 GeV) and the associated transfer lines.

    - State of the art and technical innovation

The last proton linac built in Europe was commissioned in 1988, and was based on the technology of the 70’s. The basic technology has evolved considerably since, and the present demands for high intensity operation require a vigorous R&D effort. For the last 10 years, most progress has taken place in the USA and in Japan. A high intensity pulsed proton linac is in an advanced construction phase for the Spallation Neutron Source project at the Oak Ridge National Laboratory (USA), and another one is being built in Japan (J-PARC at JAERI). The goal of the HIPPI JRA is to surpass the level of competence achieved on the other continents and provide the necessary knowledge to build world-class accelerators in Europe.

A key feature of the HIPPI JRA is the integration of the R&D for alternative technological solutions. Coordinated reporting of the progress and results will permit well controlled comparative assessments.

# Implementation plan of the joint research activity

Description of the Work Packages

Five Work Packages are outlined. Management and communication matters are covered in the first. Each of the other four Work Packages is focused on a specific technology/competence. For their definition, the participating laboratories have adapted their own work plans and baseline choices to benefit from the collective efforts and avoid duplication. Different solutions will be investigated in parallel, and their progress and achievements will be regularly communicated and discussed. Finally, comparative assessments will be published to provide elements for well-justified choices for the upgrades foreseen in the three laboratories.

Work Package 1 : Management and Communication

The following tasks are treated: oversee and coordinate the work of all work packages, organise steering committee meetings, ensure proper reviewing and reporting as well as dissemination of knowledge within the JRA and the CARE project.

Work Package 2: Normal Conducting Accelerating Structures

Normal conducting RF structures are good candidates for beam acceleration in a pulsed proton linac, up to an energy exceeding 100 MeV. This is especially true if this is the final energy, as in the case of the three foreseen upgrades, because investment in cryogenic infrastructure can be avoided. The CERN accelerator has the additional requirement to be able, with a high duty factor (14 %), to deliver a beam quality that is adequate for a cascaded high energy superconducting linac (no halo). Such differences lead to different choices of RF structures and beam dynamics, which have to be developed in parallel and experimentally compared to help optimise the designs. In the case of CERN, a classical beam dynamics is considered, and the types of structures considered are DTL (Alvarez) for the energy range from 3 to 40 MeV, Coupled Cavity Drift Tube Linac (CCDTL) for 40 to 100 MeV and probably Side Coupled Linac (SCL) above 100 MeV. Design, construction and test of prototypes are planned, to validate the technological choices and help select the economical optimum. For the GSI linac with a final energy of approximately 70 MeV, the “KONUS” beam dynamics is foreseen, with the use of H-mode structures over all the range of energies. Low power model cavities have to be built and measured, and a prototype 352 MHz CH cavity is proposed to be built and tested in a high power test stand at GSI or at CERN. Simultaneous development of these complementary structures in a single JRA will result in an optimum use of the existing infrastructure (high power RF test places, computer codes, etc.), an enlargement of the knowledge accessed by every individual contributor, and finally in a better justified choice of technological solutions in any future realisation.

Work Package 3: Superconducting Accelerating Structures

Superconducting (SC) RF cavities have much larger efficiency, accelerating gradient and bore aperture than normal conducting (NC) structures. This technology is then expected to be advantageous in a linac in terms of power consumption, construction cost and beam loss. Although this conclusion is well accepted for the high energy part of the accelerator, this is not the case at low energy, mostly because of the short distance required between transverse focusing magnets, which reduces the energy gain per real estate meter. On top of that, the Lorentz-force-induced detuning, which modulates the accelerating field in phase and amplitude, becomes larger as the lower energy. This effect has to be particularly taken into account in the case of a pulsed linac, because of the dynamic nature of the induced perturbations and of the possibility of exciting mechanical modes. It is therefore of high importance to improve the knowledge on the comparative performance of SC versus NC accelerating structures to help determine the lowest energy at which low beta superconducting cavities could safely and economically operate.

The associated critical component, required for any high intensity accelerating structure, is the input power coupler. The RF peak power transferred to the beam is typically 500 kW with duty cycles of the order of 10%, resulting also in a high average power. The peak power limitations come mainly from multipactoring and outgassing and are very frequency dependent. Couplers have to be tested up to 1 MW of forward peak power for reliability issues. High power couplers are also being developed in JRA2-WP2 for the needs TESLA but at much lower duty cycle and higher frequency. Tight links between both JRAs will be established to share the construction technology.

Three types of 700 MHz elliptical cavities will be tested in existing vertical cryostats at low power, and two of them in existing horizontal cryostats at full power. In the last test, the cavities will be fully equipped, housed in a helium tank, with tuning system and power coupler. There is presently no test site in Europe equipped with a 700 MHz high power RF source in the MW range. In the frame of this JRA, we propose to realise such a test stand at Saclay, and to make it available to the partners in HIPPI and later to any other interested European teams.

In parallel, two alternative cavity designs at 352 MHz will be analysed. Testing of two spoke-type cavities (two-gaps and multigap) is foreseen at low power, and possibly at high power, depending on the availability of a suitable infrastructure. A prototype of the tuning system for a CH resonator will built and tested.

Work Package 4: Beam Chopping

The next generation of high energy, high power proton accelerators must be designed for very low uncontrolled beam loss. In many cases, the beam from a linac is injected into a synchrotron, an accumulator or a compressor ring, and subsequently extracted. Unless suitable measures are taken to control the dynamics of the beam, both processes can lead to considerable particle loss. Loss-free injection and longitudinal capture can be achieved if the linac bunches are precisely injected inside the synchrotron buckets and no particles end-up outside. Beam loss at extraction may be minimised by ensuring that no circulating beam coincides with the field rise-time of the extraction magnet. These demands may be met by selective elimination of sets of bunches in the low energy stages of the linac by using a fast deflector or “beam chopper”. The field should rise and fall between the beam bunch interval, so that no partially chopped bunches remain in the machine, and this usually has to be within a period of the order of 2 ns.

Specifications for these key components are technically challenging, and programmes have been implemented at CERN and CCLRC-RAL based on the development of slow wave (E-field) transmission line structures and high-voltage, fast-transition time pulse generators. Differences in the programmes ensure that a range of ideas will be investigated and there will be benefits from developing each in parallel over similar timescales. Both approaches rely on two successive sets of meander-line structures, but differ in the functioning of the meander lines, in the performance requirements of the driver amplifiers and in the design of the beam dumps. Prototypes of the slow-wave structures, drivers and the beam dumps will be designed, built and tested with beam.

Work Package 5: Beam Dynamics

Recent studies with high intensity beams have shown that phenomena associated with space charge and beam loss have significant impact on the design of high power proton accelerators. In linacs, beam loss is associated largely with the appearance of a beam halo, which needs to be modelled theoretically and by simulation; it requires appropriate diagnostics and must be collimated to protect the equipment and avoid activation beyond tolerated limits. The joint activity proposed in this work package, combines resources available at the participating accelerator laboratories and universities for the analysis of the following issues:

- Validation and Benchmarking of Simulation Codes. The development of adequate 3D computer codes and the proper modelling of self-interaction by space charge is a crucial issue. Codes must be fast enough to allow large ensembles of particles in order to resolve very small loss fractions. Including the effect of errors jointly with space charge requires a significant enhancement of simulation capabilities. Benchmarking of computer simulation codes against each other and against analytical models will increase the level of confidence in their results. Strategies to minimize halo formation should result from these efforts.

- Experiments on Beam Halo and Emittance Growth. So far, no conclusive experiments on beam halo in high intensity accelerators exist; hence this issue has highest priority. Beam experiments are proposed at CERN, CCLRC-RAL and GSI, where operational conditions, available intensities and diagnostics allow relevant measurements. Their interpretation by means of simulation programs should reveal the adequacy of theoretical and simulation approaches and the methods proposed to minimize beam halo and loss.

- Diagnostics.  The acceleration and transport of high power beams also present new challenges for beam diagnostics. While conventional methods continue to be needed, operating conditions at high intensity require modification. New measurement techniques are needed to diagnose the small fractional beam losses, which could cause serious damage to components and produce unacceptable levels of activation. Monitors for direct beam halo measurements must be designed, constructed and tested in existing machines.

- Beam Collimation.  Scrapers are needed to localize beam losses in areas designed for that purpose. Injection into rings, where much less aperture is available than in linacs (in particular superconducting linacs), requires highly effective collimators prior to injection. Such schemes should be designed based on simulation data and tested in experiments.

1.2.1	Multi-annual implementation plan

The enclosed Gantt chart presents the general planning by trimester over the period 2005-2008 for each of the Work Packages. Milestones and deliverables are included. The following Pert diagrams shows the interconnections between the tasks.

1.2.2 Detailed implementation plan (Gantt chart) for the first 18 months:

# 2.	Quality of the management

# Management and competence of the participants

    - Management structure

Each Work Package has a coordinator. The JRA itself is managed by a coordinator and his deputy, who lead a steering group composed of the Work Package coordinators (see Table 2.1.1). This steering group meets every three months..

Table 2.1.1.: HIPPI management structure

| JRA coordinator | R. Garoby |  |  |
| --- | --- | --- | --- |
| Deputy | M. Vretenar |  |  |
| Work Package | Full name | Short name | Leader |
| WP1 | Management and Communication | M&C | R. Garoby |
| WP2 | Normal Conducting Accelerating Structures | NC | J.M. De Conto |
| WP3 | Superconducting Accelerating Structures | SC | S. Chel |
| WP4 | Beam Chopping | CHOP | A. Lombardi |
| WP5 | Beam Dynamics, Codes, Diagnostics and Collimation | BD | I. Hofmann |

Inside each Work Package, an annual meeting, in the form of a workshop, is foreseen to exchange and debate information between the participants. At the level of the JRA, a general meeting will be organised every year in autumn, with presentations on the main research topics. The annual report for the JRA will be published within 3 months after this event, at the beginning of the following year.

An External Scientific Advisory Committee (ESAC) will be asked to assess the progress of the various tasks and to help set up plans for the future. This committee will also help establish links with similar development programmes outside of the CARE community. Made up of 3 experts, it will participate in the annual meeting of the JRA and base its recommendations on the presentations made at that occasion.

The total effort to be invested during 5 years in the management of HIPPI is estimated to be of the order of 5 person-years.

The different teams involved and their relations are illustrated in the following synoptic.

2.1.2	Role and expertise of participants

Table 2.1.2a illustrates the participation of the different institutes in the work packages as well as the degree of integration.

Table 2.1.2a: Work Package participation

| Participant | WP1: M&C | WP2: NC | WP3: SC | WP4: CHOP | WP5: BD |
| --- | --- | --- | --- | --- | --- |
| CCLRC-RAL |  | X |  | X | X |
| CEA | X | X | X |  | X |
| CERN | X | X |  | X | X |
| FZJ |  |  | X |  | X |
| GSI | X |  |  |  | X |
| IAP-FU |  | X | X |  | X |
| INFN-Mi |  |  | X |  | X |
| CNRS-IN2P3-Orsay |  |  | X |  |  |
| CNRS-LPSC | X | X | X | X | X |

Table 2.1.2b shows the involvement of each laboratory in the different Work Packages and tasks, together with an estimate of their total contribution to the activity in person-months over the 5 years. The additional manpower support expected from the Community is included.

Table 2.1.2b : Involvement of participants

| Participant | WP/Topic | Roles | Person month |
| --- | --- | --- | --- |
| CCLRC | WP2/DTL | Beam dynamics design | 72 |
|  | WP4/Chopper B | Design and test of prototype of chopper structure and driver, 2 ns rise time, 1 kV | 96 |
|  | WP5/Development | 3D code development, parallelisation, optimisation | 30 |
|  | WP5/Benchmarking | Comparison of codes | 6 |
|  | TOTAL | Permanent staff 120, temporary staff 84 persons·month | 204 |
| CEA | WP2/DTL | Design and construction of cold model, quadrupoles and alignment system. RF measurements | 80 |
|  | WP2/CCDTL | Measurements | 2 |
|  | WP3/Elliptical | Construction alternate cavity and coupler, construction and operation of the 700 MHz test stand, tests. | 84 |
|  | WP4/Chopper line | Beam measurements | 2 |
|  | WP5/Development | Transport in 3D map, space charge compensation | 30 |
|  | WP5/Benchmarking | Comparison of codes | 10 |
|  | WP5/Experiments | Participation to the measurements at CERN | 2 |
|  | TOTAL | Permanent staff 162, temporary staff 48 persons·month | 210 |

| Participant | WP/Topic | Roles | Person month |
| --- | --- | --- | --- |
| CERN | WP2/DTL | Design of cold model, measurements | 20 |
|  | WP2/SCL | Design of model, measurements | 4 |
|  | WP2/CCDTL | Design of model, measurements | 60 |
|  | WP4/Chopper A | Design and test of pre-prototype and full prototype of chopper structure and driver, 2 ns rise time, 500 V | 36 |
|  | WP5/Development | Code preparation for 3 MeV test stand | 18 |
|  | WP5/Benchmarking | Comparison of codes | 18 |
|  | WP5/Experiments | Simulations and measurements at 3 MeV test stand | 12 |
|  | WP5/Diagnostics | Halo measurement device | 24 |
|  | WP5/Collimation | Collimator for 3 MeV line | 24 |
|  | TOTAL | Permanent staff 144, temporary staff 72 persons·month | 216 |
| FZJ | WP3/Spoke | Evaluation of 700 MHz prototype, design construction and testing of a 352 MHz b 0.48 prototype | 117 |
|  | WP5/Development | Codes preparation for SC linacs | 60 |
|  | WP5/Benchmarking | Comparison of codes |  |
|  | WP5/Diagnostics | Beam profile monitor for space charge dominated beams |  |
|  | TOTAL | Permanent staff 150, temporary staff 27 persons·month | 177 |
| GSI | WP5/Development | Improvement to codes, modelling of high current | 33 |
|  | WP5/Benchmarking | Comparison of codes | 60 |
|  | WP5/Experiments | Simulation and beam experiment at UNILAC | 93 |
|  | WP5/Diagnostics | Profile measurement by fluorescence, non-interceptive bunch measurement, online transmission control | 48 |
|  | TOTAL | Permanent staff 66, temporary staff 168 persons·month | 234 |
| IAP-FU | WP2/HDTL | H-DTL prototyping | 48 |
|  | WP3/CH | Study, design,fabrication and measurements of a prototype tuning system | 54 |
|  | WP5/Development | LORASR code | 20 |
|  | WP5/Benchmarking | Comparison of codes | 10 |
|  | TOTAL | Permanent staff 42, temporary staff 90 persons·month | 132 |
| INFN-Mi | WP3/Elliptical | Preparation test cavity with tuners (fast and slow), tests | 18 |
|  | WP5/Benchmarking | Comparison of codes | 6 |
|  | TOTAL | Permanent staff 12, temporary staff 12 persons·month | 24 |

| CNRS-IN2P3-Orsay | WP3/Spoke | Evaluation of 2-gaps 352 MHz prototypes, design and construction of coupler & tuner, test of multi-gaps prototype | 40 |
| --- | --- | --- | --- |
|  | TOTAL | Permanent staff 32, temporary staff 8 persons·month | 40 |
| CNRS-LPSC | WP2/DTL | Design of cold model, measurements | 40 |
|  | WP2/SCL | Design of model, measurements | 48 |
|  | WP2/CCDTL | Design of model, measurements | 2 |
|  | WP3/Elliptical | Contribution to cavity and coupler design | 24 |
|  | WP4/Chopper line | Beam measurements | 3 |
|  | WP5/Benchmarking | Comparison of codes | 30 |
|  | TOTAL | Permanent staff 111, temporary staff 36 persons·month | 147 |

The total effort corresponds to 1384 person-months. The expertise and relevant infrastructures of the participants are given in the Table 2.1.2c.

Table 2.1.2c: Expertise and relevant infrastructures of the participants

| Institute | Specific Expertise (indicate the expertise of the institute for that particular project) | Infrastructure relevant to the project |
| --- | --- | --- |
| CCLRC | Ion source, RFQ, chopper development. Accelerator design, construction and operation. Beam dynamics studies.. | ISIS Linac |
| CEA | Design and construction of superconducting RF systems for linear accelerators and of high-intensity normal conducting linacs. | IPHI test stand, SC laboratory |
| CERN | Design, construction and exploitation of normal-conducting linear accelerators and related equipment. Beam dynamics developments and simulations. Beam experiments. | 3 MeV test stand, Linac2 |
| FZJ | Design of superconducting accelerating structures. Design of high-intensity and high-energy accelerators. | SC laboratory |
| GSI | Linear accelerator for ion beams of high intensities, beam dynamics experiments & simulations, code development, non-destructive diagnostics for intense ion beams | UNILAC |
| IAP-FU | Linear accelerators development and construction, normal conducting and superconducting, beam optics developments and simulations. |  |
| INFN-Mi | Design and construction of superconducting RF cavities. Beam dynamics developments and simulations. | SC laboratory |
| CNRS-IN2P3-Orsay | Design of superconducting accelerating structures. Design of high-intensity and high-energy accelerators. |  |
| CNRS-LPSC | Ion sources. Accelerator design, construction and operation. IPHI collaboration. |  |

Selected references

Major references are given below. A more complete list can be found on the CARE web site.

CCLRC:

- F. Gerigk: Space Charge and Beam Halo in Proton Linacs, US-CERN-JAPAN-RUSSIA Particle Accelerator School, Long Beach, CA, 2002, http://www.isis.rl.ac.uk/acceleratortheory/frank/publications/jas02.pdf .

- M.A. Clarke-Gayther: A fast chopper for the ESS 2.5 MeV beam transport line, Proceedings of the 2002 European Particle Accelerator Conference (EPAC 2002), Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/TUPDO005.pdf .

- C.R. Prior: Computer Simulation of the Motion of Charged-Particle under Space Charge. Proceedings of Workshop on Space Charge Physics in High Intensity Hadron Rings, Shelter Island, New York. May 1998.  (CCLRC Report: RAL-TR-1998-048.)

CEA:

- J.P. Charrier et al.: 700 MHz Superconducting Proton Cavities Development and first tests in the horizontal Cryostat "CRYHOLAB", Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/THPDO036.pdf .

- N. Pichoff: Intrabeam Scattering on Halo Formation, 18th Biennial Particle Accelerator Conference, New York City, NY, USA, 29 Mar - 2 Apr 1999 - IEEE Computer Society Press, Piscataway, NJ, 1999 - http://accelconf.web.cern.ch/AccelConf/p99/PAPERS/THP135.PDF

- G. Devanz, H. Safa, C. Travier: Preliminary Design of a 704 MHz Power Coupler for a High Intensity Proton Linear Accelerator, Proceedings of EPAC 2000, Vienna, Austria, http://accelconf.web.cern.ch/AccelConf/e00/PAPERS/THP5B02.pdf

CERN:

- M. Vretenar (editor): Conceptual Design of the SPL, a High-Power Superconducting H- Linac at CERN, CERN 2000-12, http://preprints.cern.ch/yellowrep/2000/2000-012/p1.pdf

- F. Gerigk, M. Vretenar: Design of a 120 MeV H- Linac for CERN High-Intensity Applications, Proceedings of the LINAC 2002 Conference, http://linac2002.postech.ac.kr/db/proceeding/MO415.PDF

- F. Caspers, K. Hanke, A. Lombardi, A. Millich, A. Mostacci, M. Paoluzzi, M. Vretenar: Design of a chopper line for the CERN SPL, Proceedings of the LINAC 2002 Conference,

http://linac2002.postech.ac.kr/db/proceeding/MO416.PDF

FZJ:

- R. Maier et al.: The Superconducting Injector LINAC for the Cooler-Synchrotron COSY at FZ-Juelich, Proceedings of the LINAC 2002 Conference, http://linac2002.postech.ac.kr/db/proceeding/TU482.PDF

- J. Dietrich, I. Mohos, F. Wenander, G. Riehl, J. Häuser: High Sensitive Beam Emittance Analyzer, Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/THPRI115.pdf .

- Y. Senichev et al.: Some Features of Beam dynamics in super-conducting linac based on quarter- and half-wave cavities, Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/WEPLE107.pdf .

GSI:

- P. Forck and A. Bank: Residual Gas Fluorescence for Profile Measurements at the GSI UNILAC, Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/THPRI056.pdf .

- Hofmann, G. Franchetti, J. Qiang, R. Ryne, F. Gerigk, D. Jeon, and N. Pichoff: Review of Beam Dynamics and Space Charge Resonances in High Intensity Linacs, Proceedings of EPAC 2002, Paris,

http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/WEYGB001.pdf .

- W. Barth and L. Groening: Measurements and Simulations on the Beam Brilliance in the Universal Linear Accelerator UNILAC at GSI, Proceedings of the LINAC 2002 Conference, http://linac2002.postech.ac.kr/db/proceeding/TU419.PDF

IAP-FU:

- Sauer, R. Tiede, H. Deitinghoff, H. Klein, U. Ratzinger: Investigation of a Normal Conducting 175 MHz Linac Design for IFMIF, Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/THPLE059.pdf .

- A. Sauer, H. Deitinghoff, H. Klein, U. Ratzinger, R. Tiede, R. Eichhorn: Beam Dynamics Design of a Superconducting 175 MHz CH-Linac for IFMIF, Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/WEPLE081.pdf .

- R. Eichhorn, H. Liebermann and U. Ratzinger: Superconducting CH-Cavities for Low and Medium Beta Ion and Proton Accelerators, Proceedings of the LINAC 2002 Conference, http://linac2002.postech.ac.kr/db/proceeding/TU471.PDF

INFN-Mi:

- D. Barni, A. Bosotti, C. Pagani, R. Paulon, P. Pierini, H. Safa, G. Ciovati, P. Kneisel: RF Tests of the Single Cell Prototypes for the TRASCO =0.47 Cavities, Proceedings of EPAC 2002, Paris, France, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/THPDO023.pdf

- D. Barni et al.: Status of the High Current Proton Accelerator for the TRASCO Program, Proceedings of EPAC 2002, Paris, France, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/THBLA002.pdf .

- G. Bellomo, M. Novati, P. Pierini: Adiabatic Matching in Periodic Accelerating Lattices for Superconducting Proton Linacs,  Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/WEPLE109.pdf .

CNRS-IN2P3-Orsay:

- G. Olry & al.: Study of a Spoke Cavity for Low beta Applications, Proceedings of SRF2001 Workshop, September 2001, Tsukuba, http://conference.kek.jp/SRF2001/pdf/MA001.pdf

- G. Olry & al.: Design and Industrial Fabrication of a beta=0.35 Spoke-type Cavity, Proceedings of EPAC 2002, Paris,

http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/THPDO035.pdf

CNRS-LPSC:

- J.M. De Conto: GENEPI, a high intensity deuteron accelerator for pulsed neutron production, Proceedings of EPAC 1998, Stockholm, http://accelconf.web.cern.ch/AccelConf/e98/PAPERS/WEP08F.PDF .

- J.M. De Conto, C. Peaucelle: Fundamental Aspects of the Moment Problem for a Particle Density evolving under Non-linear Forces, Proceedings of EPAC 2002, Paris, http://accelconf.web.cern.ch/AccelConf/e02/PAPERS/WEPLE080.pdf .

- P.-E. Bernaudin et al.: Design of the IPHI DTL, Proceedings of PAC 2001, Chicago, USA, http://accelconf.web.cern.ch/AccelConf/p01/PAPERS/FPAH096.PDF .

2.2	Justification of financing requested

2.2.1 Detailed cost breakdown

Among the nine partners in the HIPPI JRA, six are using the Full Cost model (FC) and three the Additional Cost model (AC).

To accomplish the tasks described in section 1.2, the cost per Work Package for each contributor is given in Table 2.2.1a. Work Package 1 only covers the travel costs of the coordinators (3 per year) and of the External Scientific Advisory Committee (3 experts invited for 2 days every year)..

To help evaluate properly the means really invested in the course of the HIPPI JRA, Table 2.2.1b indicates the amount of internal resources that the institutes working under the Additional Cost model do not declare in Table 2.2.1a. They mostly correspond to the salaries of permanent staff.

The amount expected to be spent by type of expenditure is shown in Table 2.2.1c. A preliminary profile of the requested EU funding over the 5 years of the Activity is given in Table 2.2.1d.

2.2.2 Durable equipment

The HIPPI JRA includes two durable elements that can be used after its completion. Each of them has a cost which is lower than the internal laboratory contribution to the JRA activities. It can be assumed that the Community contribution will cover only the consumables, prototypes and temporary staff, while the laboratory will cover the durable equipments. These are:

- The 700 MHz high power test station at CEA-Saclay (1130 k€). A test station for pulsing superconducting cavities is essential to fully characterize the cavities developed in HIPPI, and there is none presently available in Europe. After the end of this JRA, it will be accessible to any interested institute.

- The beam diagnostics equipment at GSI, profile measurement and non-interceptive bunch measurement (110 k€). The development of appropriate diagnostics must go in parallel with the advance in beam dynamics. This device could afterwards be used in an operational accelerator.

Table 2.2.1a: Summary of expected costs and requested EU funding (kEuros)

| Acronym | Cost | WP1: M&C | WP2: NC | WP3: SC | WP4: CHOP | WP5: BD | Total |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Model | Exp. Cost | Req. Cost | Exp. Cost | Req. Cost | Exp. Cost | Req. Cost | Exp. Cost | Req. Cost | Exp. Cost | Req. Cost | Exp. Cost | Req. Cost |
| CCLRC | FC | 0 | 0 | 855 | 200 | 0 | 0 | 1 663 | 200 | 614 | 65 | 3 132 | 465 |
| CEA | FC | 11 | 11 | 684 | 119 | 2 715 | 800 | 0 | 0 | 425 | 50 | 3 835 | 980 |
| CERN | AC | 65 | 65 | 770 | 340 | 0 | 0 | 400 | 130 | 300 | 100 | 1 535 | 635 |
| FZJ | FC | 0 | 0 | 0 | 0 | 1 580 | 365 | 0 | 0 | 695 | 162 | 2 275 | 527 |
| GSI | FC | 16 | 11 | 0 | 0 | 0 | 0 | 0 | 0 | 1 665 | 352 | 1 681 | 363 |
| IAP-FU | AC | 0 | 0 | 436 | 180 | 385 | 165 | 0 | 0 | 183 | 75 | 1 004 | 420 |
| INFN-Mi | AC | 0 | 0 | 0 | 0 | 190 | 77 | 0 | 0 | 3 | 3 | 193 | 80 |
| CNRS-IN2P3-Orsay | FC | 0 | 0 | 0 | 0 | 272 | 70 | 0 | 0 | 0 | 0 | 272 | 70 |
| CNRS-LPSC | FC | 11 | 11 | 490 | 46 | 120 | 0 | 15 | 0 | 170 | 3 | 806 | 60 |
| CNRS total | FC | 11 | 11 | 490 | 46 | 392 | 70 | 15 | 0 | 170 | 3 | 1 078 | 130 |
|  |  |  |  |  |  |  |  |  |  |  |  | 14 733 | 3 600 |

2.2.1b: Internal cost not accounted for in Table 2.2.1a for participants using the AC model (kEuros)

| Acronym | Cost Contribution |
| --- | --- |
| CERN | 1 350 |
| IAP-FU | 288 |
| INFN-Mi | 47 |
| Total | 1 685 |

Table 2.2.1c: Costs per participant

| Laboratory | CCLRC-RAL | CEA | CERN | FZJ | GSI | IAP-FU | INFN-Mi | CNRS-IN2P3-Orsay | CNRS-LPSC | CNRS total |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Cost model | FC | FC | AC | FC | FC | AC | AC | FC | FC | FC |
| Durable equipment | 0 | 1 065 | 0 | 0 | 110 | 0 | 0 | 0 | 0 | 0 |
| Consumables & prototypes | 550 | 924 | 660 | 245 | 0 | 450 | 123 | 130 | 55 | 185 |
| Temporary Staff | 788 | 200 | 810 | 304 | 680 | 540 | 40 | 15 | 65 | 80 |
| Permanent Staff | 1 779 | 1 635 | / | 1 696 | 865 | / | / | 120 | 675 | 795 |
| Travels | 15 | 11 | 65 | 30 | 26 | 14 | 30 | 7 | 11 | 18 |
| Total | 3 132 | 3 835 | 1 535 | 2 275 | 1 681 | 1 004 | 193 | 272 | 806 | 1 078 |
| Requested contribution | 465 | 980 | 635 | 527 | 363 | 420 | 80 | 70 | 60 | 130 |

Table 2.2.1d: Preliminary profile of requested EU funding over JRA duration

|  | 2004 | 2005 | 2006 | 2007 | 2008 | Total |
| --- | --- | --- | --- | --- | --- | --- |
| CCLRC | 84 | 88 | 93 | 97 | 103 | 465 |
| CEA | 210 | 240 | 480 | 48 | 2 | 980 |
| CERN | 80 | 150 | 195 | 150 | 60 | 635 |
| FZJ | 90 | 140 | 160 | 100 | 37 | 527 |
| GSI | 130 | 80 | 100 | 40 | 13 | 363 |
| IAP-FU | 75 | 141 | 132 | 36 | 36 | 420 |
| INFN-Mi | 20 | 20 | 30 | 8 | 2 | 80 |
| CNRS-IN2P3-Orsay | 5 | 10 | 20 | 20 | 15 | 70 |
| CNRS-LPSC | 2 | 20 | 30 | 6 | 2 | 60 |
| CNRS total | 7 | 30 | 50 | 26 | 17 | 130 |
| Total | 696 | 898 | 1249 | 499 | 258 | 3600 |

# 3.	European added value

# 3.1 	Interest for European research infrastructures and their users

The R&D effort in HIPPI will be the basis for improvements at three major European laboratories, broadening at the same time their potential for physics and the size of the interested scientific community.

These upgrade programmes pursue different and complementary goals:

- Neutrino physics (represented in CARE by the NA3): the community has shown a substantial interest in the proposed upgrades at CCLRC-RAL and CERN [1]. With the support of ECFA, a series of  workshops (“NuFact”), started in Lyon in 1999, has since taken place every year in various places around the world. The proton driver is an important subject, addressed at each occasion, where progress is eagerly expected.

- Radioactive ion physics: the ISOLDE experiments at CERN would immediately benefit from the higher proton flux from an improved injector [2]. Furthermore, the EURISOL study [3], supported by NuPECC, has shown that the next generation facility using the Isotope on line separation technique  needs a two orders of magnitude larger proton flux. The upgrades considered in the HIPPI JRA could constitute a first step towards the necessary proton driver.

- Spallation Neutron sources: since the interruption of the ESS project, this programme is now continuing mainly as an upgrade of the ISIS facility at CCLRC-RAL [4].

- Upgrade of the Large Hadron Collider (represented in CARE by NA3 and JRA5): the upgrade of the CERN injector complex is a logical first step towards a performance upgrade of the LHC [5].

Considering the magnitude of the resources that the European countries have already devoted to the construction of the CERN, GSI and CCLRC-RAL complex of accelerators, these improvements would significantly increase their potential value for physics research in the future for a marginal additional cost.

# 3.2	Exploitation of results

The results of the HIPPI JRA will consist in the development of new technologies for the design and construction of high intensity pulsed linear accelerators. The prototypes, the calculation tools and more generally the expertise developed in this frame will be the basis for the design and construction of the next generation of accelerators in Europe. They will be exploited in priority by the three laboratories interested in upgrading their accelerator complex.

However, the outcomes of HIPPI will not be patented, and according to the policy of the partner institutions, will be available to the scientific community and to industrial companies interested in accelerators for technological applications (generation of radio-isotopes for medicine, biology …).

The reports produced in the frame of HIPPI will be referenced and will be accessible through the scientific information distribution system of the partner laboratories. Part of the reports, integrally or in a condensed form, will be published in scientific journals and in the proceedings of international conferences.

# 3.3	Risk assessment

Monitoring success

The specifications to be met by the various prototypes will be defined at the general meeting of HIPPI in the autumn 2004, with the approval of the External Scientific Advisory Committee. The ambition is to surpass the performance of the machines presently under construction in the US or in Japan. Success will be measured by the degree at which these technical goals are met. An important parameter to evaluate the technical solutions will be their cost, which has to be smaller or equal (for a better performance) to that of the previous generation of European linear accelerators.

The most challenging goals are summarized as follows:

- in WP2 (normal-conducting accelerating structures): development of high-current structures less expensive than conventional DTL’s, while keeping a shunt impedance ZT2 (power efficiency) higher than 40 M/m in the energy range 20-100 MeV. At lower energy (3-20 MeV), the challenge is to develop a low cost DTL design.

- in WP3 (superconducting accelerating structures): development of structures that reach a gradient exceeding 7 MV/m with Q 1010 in the energy range 100-200 MeV, at a construction cost comparable to normal-conducting structures.

- in WP4 (chopping): development of a chopping set-up (chopper and chopper-line) leaving no partially filled buckets [switching time smaller than the distance between bunches at 352 MHz (CERN goal) or 280 MHz (RAL goal), limited overshoot and ringing, …]. Moreover, the overall design of the chopper-line has to minimize emittance growth.

- in WP5 (beam dynamics): experimental validation of simulation codes, and rules for a beam optics design, including collimators and appropriated diagnostics tools, capable of keeping the uncontrolled beam loss below the threshold for hands-on maintenance (1 W/m) all along a high energy linac (> 1 GeV) and the associated transfer lines.

Impact

Apart from the three foreseen accelerator upgrades in Europe, it is foreseeable that the outcome of the HIPPI JRA will become a reference for the next projects elsewhere in world. Other impact will include the education of young scientists in the field of accelerator technology and the reinforcement of links between European institutions.

Risk

The general approach of the HIPPI JRA is to develop in parallel different technologies of diverse complexity and/or innovative content, with the aim of finally providing comparative assessments. Since it is very unlikely that all approaches will fail simultaneously, the risk of complete failure is very low. Using the definitions given in Table 3.3a, the list of tasks with an associated risk are listed in Table 3.3b. In each case, a corrective action is indicated as well as the consequences on the project.

Table 3.3a : Definition of risk levels

| Risk Level | Meaning |
| --- | --- |
| RL1 | Low Risk: minor error might happen, could be easily corrected since no technical challenge is involved. Scope of the project is unchanged. Minor impact on schedule (<3 months) or cost (<5%) might be necessary. |
| RL2 | Medium Risk: A small downgrading of the final objectives might be required. Alternatively a small delay (<1 year) and cost increase might be necessary (<20%) to maintain the initial objectives. |
| RL3 | High Risk: Significant downgrading of the objectives might be required. Alternatively more R&D, more time (>1 year) and more money (>20%) would be required. |

Table 3.3b : Risk assessment

| WP | Topic | Risk | Action | Level | Consequence |
| --- | --- | --- | --- | --- | --- |
| 1 | DTL | One or more of the proposed design improvements do not work | Add more time for development or revert to standard construction technique (CERN Linac2) | 1 | Delay / Extra cost for construction |
| 1 | HDTL | The prototype presents tuning/cooling problems or does not have the design efficiency | Revert to other structures requiring more RF Power (DTL, CCDTL, SCL) | 1 | Extra cost for construction |
| 1 | SCL | Not able to tune the cold model | New cold model with revised design | 1 | Delay to 12/08 |
| 1 | CCDTL | The prototype presents tuning/cooling problems | Revert to a DTL design, requiring more RF power | 1 | Extra cost for construction |
| 2 | Elliptical | A satisfactory gradient under pulsed tests is not achieved by end 2008 | If the other SC developments fail, adopt a normal conducting design for all the linac | 1 | None |
| 2 | Spoke | A satisfactory gradient is not achieved by end 2008 | If the other SC developments fail, adopt a normal conducting design for all the linac | 1 | None |
| 2 | CH | Problems in cooling or in achieving a satisfactory gradient | If the other SC developments fail, adopt a normal conducting design for all the linac | 1 | None |
| 3 | Chopper A | Prototype not achieving specified rise time or voltage | If also chopper B fails: accept some loss level in the machine | 2 | Degradation of machine performance |
| 3 | Chopper line | Emittance growth and/or beam loss measured in chopper line | Accept some loss level in the machine | 2 | Degradation of machine performance |
| 3 | Chopper line | Chopper dump prototype performance not to specifications | Limit operation to low duty cycle (<1%) | 1 |  |
| 3 | Chopper B | Prototype not achieving specified rise time or voltage | If also chopper A fails: accept some loss level in the machine | 2 | Degradation of machine performance |
| 4 | Simulation codes | Failure of the codes to represent measured parameters at the test stand | Accept some loss level in the machine | 2 | Degradation of machine performance |
| 4 | Beam experiment | Diagnostics not ready in time, not providing the required resolution | Additional development required | 1 | Delay ( ~1 year) |

REFERENCES (section 3)

[1] Web-site for “Neutrino Factory and Muon storage rings at CERN”, http://muonstoragerings.web.cern.ch/muonstoragerings/

[2] M. Lindroos: Future Plans at ISOLDE, 14th International Conference on Electromagnetic Isotope Separators and Techniques related to their Application, 6-10 May, 2002, Victoria, BC,

Canada, http://doc.cern.ch/archive/electronic/cern/preprints/ps/ps-2002-047.pdf

[3] Web-site of the EURISOL study, http://www2.ganil.fr/eurisol/index.html

[4] Web-site of the ESS study, http://www.ess-europe.de/en/index.php

[5] LHC Luminosity and energy upgrade : A Feasibility Study / O. Bruning et al. 
CERN-LHC-Project-Report-626 ; LHC-Project-Report-626. - Geneva : CERN , 1 Dec 2002. - 98 p. - Fulltext