NEW YORK OCEANIC FIR DATA LINK PROCEDURES

New York ARTCC offers full CPDLC capability within the entire New York Oceanic FIR for FANS-1/A capable aircraft. The New York Oceanic FIR log-on address is “KZWY”.

1. Log-On

- Aircraft entering the New York Oceanic FIR from adjacent non-CPDLC airspace:

1.  Log on to CPDLC at least 15 minutes but not more than 45 minutes prior to entering the New York Oceanic FIR.

2.  PRIOR to entering the New York Oceanic FIR contact ARINC on HF providing the            information as outlined in section 2 below.

- Aircraft entering the New York Oceanic FIR from adjacent CPDLC airspace: Pilots should determine the status of the CPDLC connection when crossing the New York Oceanic FIR boundary.

1.  If “KZWY” is the active connection, when crossing the New York Oceanic FIR

boundary the pilot shall;

a.   Contact ARINC on HF providing the information as outlined in section 2 below.

  - If “KZWY” is not the active center, when crossing the New York Oceanic FIR boundary the pilot shall;

      - Terminate the CPDLC connection, then log-on to “KZWY”.

      - Contact ARINC on HF providing the information as outlined in section 2 below.

2. High Frequency (HF) Communications Requirement

As required above when contacting ARINC on HF or VHF:

1.  Identify the flight as CPDLC equipped.

2.  Provide the FIR exit point and the name of the next controlling facility.

3.  State the track letter if operating on the organized track system (OTS).

4.  Request a SELCAL check and expect to receive primary and secondary HF frequency assignments from ARINC. ARINC will then require flights transiting 60W longitude to contact them at 60W for HF frequency updates.

NOTE 1: 	HF frequency updates are required due to frequency propagation.

NOTE 2: 	Pilots must maintain HF communications capability with ARINC at all

times within the New York Oceanic FIR.

Example Transmissions

Random Route:

“New York Radio, (call sign), CPDLC, exit point (SUMRS), (Miami) next, SELCAL (AB-CD).”

Organized Track:

“New York Radio, (call sign), CPDLC, NAT Track (Whiskey), exit point (44N50W), (Gander) next, SELCAL (AB-CD)”

3. Flights Over Flying Bermuda Airspace

Prior to entering Bermuda airspace, aircraft will receive an END OF SERVICE message that will result in termination of CPDLC. Aircraft shall re-log-on to “KZWY” prior to re-entering the New York Oceanic FIR when they are advised by ATC to contact ARINC on HF.

4. Position Reports

When logged on to “KZWY”, normal waypoint position reports will be received via ADS (if so equipped). Operators should not use CPDLC for position reports when using ADS, unless requested to by ATC. Use CPDLC for clearance requests, and for communications not associated with position reports. “KZWY” CANNOT accept CPDLC position reports containing latitude/longitude in ARINC 424 format (e.g. 4050N).

5. Controller Pilot Data Link Communications (CPDLC) Failure

In the event of Data Link failure or outages, flight crews shall contact New York Radio via HF voice for routine communications. SATVOICE contact should be limited to distress and urgency situations.

6.  Questions

Direct questions to the New York Center Airspace and Procedures Office, telephone: 001-631-468-1018, fax 001-631-468-4229 during normal business hours, Monday – Friday. During all other times, contact the New York Center North Atlantic Supervisor: 001-631-468-1496, or Aeronautical Radio Supervisor: 001-631-244-2483. Additional information concerning CPDLC can be found at: http://www.faa.gov/ats/ato/130.htm

(Oceanic Operations Standards Group (AJE-32), 5/31/06)