JRG-29

March 22, 2005

User’s Manual for ITU-R Radar Emission Mask Spreadsheet

1. Introduction

The ITU-R Emission Mask spreadsheet will plot the permitted emission limits for primary radar stations operating in the radiodetermination service as required in Appendix 3 of the Radio Regulations for spurious emissions limits and the recommended out-of-band emission limits as described in Recommendation ITU-R SM.1541 Annex 8.  In addition, measured emission spectrum data can be imported into the spreadsheet for comparison with the ITU-R emission limits.  The ITU-R Emission Mask spreadsheet is in Microsoft Excel format.

A User’s Manual for the spreadsheet is available by clicking on the HELP button.  For the HELP button to work, the associated HELP file must be in the same folder as the Excel spreadsheet.

Comments and suggested improvements to the spreadsheet should be sent to Robert Sole at rsole@ntia.doc.gov.

2.  System Requirements

To run the ITU-R Emission Mask spreadsheet, your Personal Computer (PC) must have Excel 2000 or later version, and your PC should have Windows 98 or later operating system.

3. Opening Program

Bring-up Microsoft Excel on your PC.  Open the program ITU-R Emission Mask.  Enable the macros (you will be prompted to do this task).  If not prompted to enable macros, then go to the Tools pull down menu, select Macro-Security. In the Security level tab, choose Medium and press OK.  Close the spreadsheet and re-open it.  Upon re-opening the spreadsheet, you should be prompted to enable Macros.

Click on the NEW/Restart button to initialize the spreadsheet.

4. Importing Measured Emission Spectrum Data

Measured emission spectrum data may be imported into the program.  If measured data is being used, it should be imported prior to providing the data in Table 1 since the Excel program determines some parameters in Table 2 from the measured emission spectra data.  If measured data is not being imported, only ITU-R emission mask is being plotted, go to Section 6.

Sample emission spectrum data is available to validate the model.  See procedures below for importing sample measured data.

The imported emission spectrum data files must be in an ASCII coma, space or tab delimited format; Easy Plot file format, or table entry.  For the ASCII format, the data must include the emission spectrum data in two fields: 1) frequency in MHz, 2) measured emission spectrum data in absolute power (e.g.; dBW or dBm), or in dB relative to the maximum measured signal level.  Note: if the data is in absolute power the program will normalize the data to dB relative to the maximum measured signal level.

The procedure for importing measured data into the spreadsheet is as follows.

- Click on the Get Data button.

- A Emission Spectrum Data window will pop-up.  Click on the Read/Describe Emission Spectrum Data button.

- A Emission Spectrum Input window will pop-up. Click on the Read ASCII (CSV) File button if the emission spectrum data is in an ASCII file.  Click on the Read EP File button if the emission spectrum data is in an Easy Plot file.  If the spectrum data is not in a file, and is available in a Table Entry form, click on Table Entry.  If you want to import one of the sample data files, click on the sample aeronautical or maritime data button.

- An Open Emission Spectrum Data File window  will pop-up. Go to the bottom of the menu and where it says “Files of type”, use the pull-down menu to select “all files.”  Locate the file to be imported into the spreadsheet using the Look in pop-down button.  Select the file to be imported, and click on Open.

- Click on the OK button in the Open Emission Spectrum Input window.

- A window will come on the screen that says Emission Spectrum Data with the ability to select fixed frequency or frequency hopping.  Select the appropriate radar mode, fixed frequency or frequency hopping.  If you select fixed frequency, window will display the Operating Frequency (FO) based on the measured data.  If you select the Frequency Hopping Mode, the Lowest Channel Frequency (FL) and Highest Channel Frequency (FH) windows will display the selected FL and FH frequencies based on the measured data.  In cases where there are multiple operating (fundamental) frequencies, or the radar is a frequency hopping radar, the program may not select the appropriate Operating Frequency (FO), or in the case of frequency hopping radar the Lowest Channel Frequency (FL) and Highest Channel Frequency (FH) for plotting the ITU-R emission mask.  If the appropriate FO, FL , or FH values were not selected, type in the appropriate values.    Then click the OK   button.  Measured data should now be visible on the Spread Sheet.  The Excel program will normalize the power level at the fundamental frequency (FO) to 0 dB.  Verify that the FO data in Row 6 of the spread sheet is in agreement with the plotted data.  In the case of frequency hopping radars, the value for FO in Row 6, should be midway between FL and FH.

- If desired, the frequency scale of the measured data can be normalized to Zero MHz/GHz at the radar Fundamental Frequency (FO).  Verify that the value to normalize the measured data to in Row 6 is correct.  Click on the Normalize to FO button in Row 53.  The measured data will be normalized to FO is zero Hertz.

5.  Changing Graph Title and X and Y Axis.

Once the measured data has been imported into the spreadsheet, the Titles and the X and Y axis range on the measured data plot can be changed if necessary.

A. The graph titles, and X and Y axis titles can be changed by clicking on the Set Graphs Titles button.  Make appropriate changes to the titles, and click on the OK button.

- The scale range of the X and Y axes can be changed if necessary by pointing the mouse to the X or Y scale on the graph and right click when the Values (X or Y) axis window pop-up.  Then click on Format Axis.   A Format Axis window will pop-up.  Click on the Scale tab, and change the axis values as required.  If you change the Y axis to a more negative number (e.g., -120 to -140) it will be necessary to also change the  Value the X axis crosses at to -140.  Then click on the OK button.  The measured data should now be in the desired format.

6.  Importing ITU-R Emission Mask

To develop and import the ITU-R emission mask for particular radar characteristics follow the steps below.

A.  Peak Envelope Power and Measurement Bandwidth

1.	Type in the radar Peak Envelope Power (PEP) in Row 7 of the spreadsheet.  The Pop-Down window to the right lets you select appropriate units for specifying PEP.  Click on the units then click on the Pop-Down window to change the units.

2. Type in the measurement bandwidth (Bm) in Row 9 of the spreadsheet.  The measurement bandwidth (Bm) should be in the units of MHz.

B.  Table 1 – Pulse/Sub-Pulse Characteristics

Table 1 is provided to input the measured or calculated pulse/sub-pulse characteristics for determining the ITU-R emission mask limits.  The definition of the radar parameters in Table 1 are provided in Recommendation SM.1541, Annex 8. Table 2 shows the calculated ITU-R emission mask parameters and other data needed for emission mask and measured data correction factors for the radar parameters entered in Table 1.

The Table 1 spread sheet will let you specify up to eight pulse/sub-pulse time waveform characteristics for multiple waveform radars.  For multiple waveform radars, the ITU-R emission mask limits are determined from the pulse type (waveform) which results in the maximum B-40 dB bandwidth (see Recommendation ITU-R SM.1541, Section 3.1).

Use the following procedure for providing the pulse/sub-pulse waveform information in Table 1.

A.	The column labeled Pulse Type must have a value selected. Place the cursor at the small red triangle on the upper right side of the cell for guidance on selecting the proper pulse type.  There are nine pulse/waveform modulation types to choose from.  Type in the appropriate number.  Once the pulse type is determined, fields in Table 1 that are not applicable to that pulse type will have an NA in them.

B.	The column labeled Pulse Width or Sub-Pulse Width (t) must have data entered into it for the pulse width in microseconds.  Place the cursor on the small red triangle on the upper right side for guidance for determining the pulse width.

C.	The column labeled Pulse Rise/Fall Time (tr) must have data entered into it for the rise time in microseconds.  Place the cursor on the small red triangle on the upper right side for guidance for determining the pulse rise time.

D.	For frequency swept (chirped) pulses, the column labeled Chirp Bandwidth (Bc) must have data entered into it for the chirp range in MHz.  Place the cursor on the small red triangle on the upper right side for guidance for determining the chirp bandwidth.

E.	For CW radars, the column labeled Total Frequency Deviation (Bd) must have data entered into it for the frequency deviation range in MHz.  Place the cursor on the small red triangle on the upper right side for guidance for determining the frequency deviation.

F.	For phase coded pulses, the column labeled Number of Chips per Pulse (N) must have data entered into it for the total number of chips per pulse.  Place the cursor on the small red triangle on the upper right side for guidance for determining the number of chips.

G.	For frequency hoping radars, the columns labeled Lowest Channel and Highest Channel Frequency (FL and FH) must have data entered into it for the lowest and highest channel frequency of a frequency hopping radar deviation in MHz.  Place the cursor on the small red triangle on the upper right side for guidance for determining the frequency deviation.

After the radar characteristics data has been completed in Table 1, the calculated parameters related to the ITU-R Emission Limits Mask, and measured data correction factors are shown in Row 1 of Table 2.

7.  Plotting ITU-R Emission Mask

Review the calculated parameters related to the ITU-R Emission Limits Mask data, and measured data correction factors shown in Table 2.  The ITU-R Emission Mask can be plotted on the measured data using the following procedure.

- The emission mask data that will be plotted over the measured data corresponds to the Emission Mask Number shown in Column A of Table 2.  If the radar mode has multiple pulse waveforms, review the B(-40 dB) bandwidths shown in Table 2 for the various pulse waveforms. Check the mask number shown in Row 38.  If necessary, change the mask number in Row 38 to corresponds to the Emission Mask number in Column A of Table 2, which has the maximum B(-40 dB) bandwidth.  Click on the Add/Del Mask button shown in Row 40.  The emission mask will be added in the plot.

B.	To delete the emission mask from the plot, click on the Add/Del Mask button shown in Row 40.   Check the mask number shown in Row 38.  If necessary, change the mask number in Row 38 to corresponds to the Emission Mask number that you want to delete shown in Column A of Table 2.

C.	To plot a second mask on top of the existing mask with a different slope (dB/decade) from the  B(-40 dB) bandwidth, click the appropriate Waveform number in TABLE 1 and then click on the Copy Row button.   A new row with data will appear in tables 1 and 2.  Change Slope (db/decade) field in Table 2 to the desired value.  Check the mask number shown in Row 38.  If necessary, change the mask number in Row 38 to correspond to the Emission Mask number that you want to change the slope of shown Table 2.  Click on the Add/Del Mask button shown in Row 40.  The second emission mask will be added in the plot.

8.	ITU-R Mask Offset

Recommendation ITU-R SM.1541, Section 4, states that B -40 dB bandwidth can be offset from the frequency of maximum emission level and can be shifted to center the mask at the measured -40 dB level of the measured data.  If there is a ITU-R Mask on the Graph, click on the Add/Del Mask button.  This will delete the indicated mask.  To offset the ITU-R mask, click on the Mask Offset button and type in the desired frequency shift in a positive or negative direction.  Then click on the Add/Del Mask button.  The shifted ITU-R emission mask should appear, and the OOB/Spurious Domain Intercept Frequencies in Table 2 should be changed by the amount of frequency shift.

9.  Plotting Additional Emission Masks

Additional emission masks with parameters other than the ITU-R Emission Mask can be plotted on the measured data.  To plot additional emission masks to the data plot, it is necessary to provide additional Pulse/Sub pulse characteristics data in another row of Table 1.  This can be accomplished by clicking on the row in Table 1 that you want copied, and then click the Copy Row button, rows 22-23.  The RSEC Emission Mask data will appear in the corresponding row in Table 2.  Change the appropriate parameter (e.g.; Slope dB/dec,) in the row of Table 2.  Change the Mask Number in Row 38 to the appropriate row of Table 2.  Click on the Add/Del button shown in Row 40.  The additional emission mask will be added in the plot.

10.  Printing of Spreadsheet

To print Table 1, Table 2, and the graph click on the Summary button on line 3 (Note: you must click on the Summary button on line 3 to import the data prior to clicking on the Summary tab at the bottom of the page).  From the Summary page, the spread sheet can be printed, or copied to a text document.

11.  Viewing of Measurement Data and ITU-R Emission Mask Data

To view the measurement data and ITU-R emission mask data, click on the Temp tab at the bottom left of the excel screen.

SAMPLE DATA 1

Aeronautical Radionavigation Radar

| F0 | 2844.4 | MHz |
| --- | --- | --- |
| PEP | 1.300 | Megawatts |
| Bm | 1 | MHz |

Table 1

Pulse/Sub-pulse Characteristics

| Waveform Number | (t) Pulse Width or Sub-Pulse Width (u sec) | (tr) Pulse Rise/ Fall time (u sec) | (Bc) Chirp Band width (MHz) | (Bd) Total Frequency Deviation | (N) Number of Chips Per Pulse | (FL) Lowest Channel Frequency (MHz) | (FH) Highest Channel Frequency (MHz) | Pulse Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.6 | 0.05 | NA | NA | 1 | NA | NA | Non-FM pulsed radars |
| 2 | 0.6 | 0.05 | NA | NA | 1 | NA | NA | Non-FM pulsed radars |

Table 2

Calculated Results

| Emmision Mask Number | (Bs) Frequency Hopping Range (MHz) | (BPEP) Required Bandwidth to Measure PEP (MHz) | (Bref) Reference Bandwidth (MHz) | K Coefficient | B(-40) Bandwidth (MHz) | (S)* Slope (dB/dec) | RR Appendix 3 Spurious Attenuation (dB) | OOB/ Spurious Domain Intercept Freq (MHz) | Spurious Domain Correction (dB) Mask / Data |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0 | 1.667 | 1.000 | 6.20 | 35.796 | 20.00 | -60.00 | 2665.42 3023.38 | -55.56 0. |
| 2 | 0 | 1.667 | 1.000 | 6.20 | 35.796 | 40.00 | -60.00 | 2787.80 2901.00 | -55.56 0. |

SAMPLE DATA 2

Maritime Radionavigation Radar

| F0 | 9406 | MHz |
| --- | --- | --- |
| PEP | 12.000 | Kilowatts |
| Bm | 1 | MHz |

Table 1

Pulse/Sub-pulse Characteristics

| Waveform Number | (t) Pulse Width or Sub-Pulse Width (u sec) | (tr) Pulse Rise/ Fall time (u sec) | (Bc) Chirp Band width (MHz) | (Bd) Total Frequency Deviation | (N) Number of Chips Per Pulse | (FL) Lowest Channel Frequency (MHz) | (FH) Highest Channel Frequency (MHz) | Pulse Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0.83 | 0.02 | NA | NA | 1 | NA | NA | Non-FM pulsed radars |

Table 2

Calculated Results

| Emission Mask Number | (Bs) Frequency Hopping Range (MHz) | (BPEP) Required Bandwidth to Measure PEP (MHz) | (Bref) Reference Bandwidth (MHz) | K Coefficient | B(-40) Bandwidth (MHz) | (S)* Slope (dB/dec) | RR Appendix 3 Spurious Attenuation (dB) | OOB/ Spurious Domain Intercept Freq (MHz) | Spurious Domain Correction (dB) Mask / Data |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0 | 1.205 | 1.000 | 7.60 | 58.987 | 20.00 | -60.00 | 9111.06 9700.94 | -58.38 0. |
| 2 |  |  |  |  |  |  |  |  |  |

# Footnotes

Procedures for guiding measurement of radar emission spectra for determining compliance with ITU-R Radio Regulation Appendix 3 and Recommendation ITU-R SM.1541 should be in accordance with Recommendation ITU-R m.1177, Techniques for measurement of undesired emissions of radar systems.