Poster Presentation 3-10

Production of Butanol from Concentrated Lactose/Whey Permeate Using Clostridium acetobutylicum and Removal by Perstraction

N. Qureshi1* and I.S. Maddox2

1University of Illinois

Biotechnology & Bioengineering Group

Department of Food Science

1207 W Gregory Dr. Urbana, IL 61801

Phone:	(217) 244-6354; Fax: (217) 244-2517; E-mail: nqureshi@uiuc.edu

2Institute of Technology and Engineering

Massey University

Palmerston North, New Zealand

Acetone-butanol-ethanol (ABE) were produced from whey permeate medium, supplemented with lactose, in a batch reactor using Clostridium acetobutylicum P262, coupled with ABE removal by perstraction.  ABE (87.2 g/L) were produced from lactose (277 g/L) at a yield of 0.43 and productivity of 0.22 g/L.h.  These results are superior to ABE batch fermentation where a maximum ABE concentration of 20 g/L is achieved. Silicone tubing (membrane area 0.1130 m2 based on inside diameter) was used as the perstraction membrane while oleyl alcohol was used as the perstraction solvent.  Removal of ABE by perstraction was faster than their production in the reactor, and the maximum concentration of ABE in the oleyl alcohol was 7.5 g/L.  However, the fermentation ceased prior to complete lactose utilization, probably due to back-diffusion of oleyl alcohol into the fermentation medium.  Hence, perstraction compares unfavourably with gas stripping (Maddox et al. 1995) as the product removal technique in integrated batch fermentation/product removal processes utilizing high sugar concentrations.

Reference:

Maddox IS, Qureshi N, Roberts-Thomson K (1995) Production of acetone-butanol-ethanol from concentrated substrates using Clostridium acetobutylicum in an integrated fermentation-product removal process. Process Biochem. 30: 209-215