UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON, D.C. 20460

OFFICE OF

PREVENTION, PESTICIDES AND

TOXIC SUBSTANCES

April 4, 2006

MEMORANDUM

SUBJECT:	Sodium cyanide: Occupational Exposure Assessment and Recommendations for the Tolerance Reassessment Eligibility Decision (TRED) Document  (RED Case 2560)

FROM:		David Jaquith, Environmental Scientist

Reregistration Branch 4

Health Effects Division

THRU:	Susan Hummel, Senior Scientist

Reregistration Branch 4

Health Effects Division

TO:		Rebecca Daiss, Risk Assessor

Reregistration Branch 4

Health Effects Division

Craig Doty, Chemical Review Manager

Special Review and Reregistration Division

DP Barcode(s):	D318017

PC Code: 		074002

MRID				46648901

###### 1.0		Background and Purpose

The attached document addresses occupational exposures and risks for sodium cyanide oxide to support the Health Effects Division (HED) reregistration eligibility decision (RED) document. A RED was completed in September 1994 (pre FQPA, ORE Chapter February 28, 1994) but the RED did not consider the use for fumigation of citrus.  A Phase IV review was completed June 19, 1992 and did not consider the fumigant use.

## Products and Formulations

Sodium cyanide exists in two formulations; predator baits and for fumigation of citrus shipped from California to Arizona.  The application rates are presented in Table 1.  A more detailed summary of the labels is presented in Appendix A.

Application Rates

| Table 1: Sodium Cyanide Application Rates |
| --- |
| Scenario | Application Rate | Fumigation Time (hours) |
| Fumigation of Citrus Fruit | 1 oz/100ft3 of Sodium Cyanide (Equivalent to 6 oz HCN/1000 ft3 | 1 hour |
| Animal Baits/Injectors | 91.06 % sodium cyanide per bait, up to 10-12 units per square mile | NA |

###### Fumigation Process

Sodium cyanide is registered in California as Special local need (SLN CA-840006) for the generation HCN to fumigate citrus eliminate red scab another surface pests prior to shipment to Arizona.  It is used as quarantine procedure to prevent the spread of these pests. Trailers are fumigated with HCN using a closed system in which the appropriate amount of sodium cyanide is mixed with concentrated sulfuric acid and water.  The trailers are fumigated for 1 hour.  They are then aerated with more than 10 air changes for ½ or 1 hour.  The results of an air monitoring are presented in Appendix B.

###### Bait Process

The use of sodium cyanide in bait products has been discussed in the RED document in September 1994 and the ORE chapter for the review (W. Dang, February 28, 1994) and will not be further considered in this report.

3.0		Hazard Identification

Cyanide is an acute toxicant.  However, with the exception of citrus fumigation the Agency has relied on incidence data to identify any hazard associated with use of this compound.  These data are compiled in the following section.

4.0		Incident Report

Only 5 reports have been submitted by USDA APHIS concerning mishaps with M-44 Capsules containing sodium cyanide since 1992 when EPA set up the Incident Data System.  None of the mishaps resulted in serious medical outcomes.  All resulted in transient symptoms which were minor to moderate.  Poison Control Centers have tracked rodenticide use of cyanide over the years since 1985, however, their system does not specify the form of the cyanide (e.g., calcium cyanide, sodium cyanide, or hydrogen cyanide).  On average Poison Control Centers receive only one report per year.  Most listed the outcome as not determined or, at most, minor medical outcome. (Jerry Blondell, 2005)

5.0		Non-Occupational/Residential Exposure

.	This material is not used in the residential environment

Label Requirements

The end-use label for fumigation (EPA Reg. No. 39352-50001-AA) requires the following regarding exposure and worker protection.

- Where there is potential for dermal contact, full body personal protective equipment (PPE) must be worn.  This includes solvent-proof gloves, clothing, hat, apron, and boots.  Vapor-proof goggles are also required.

6.1		Non-Cancer and Cancer Occupational Exposure and Risk Estimates

Short-/Intermediate-Term and Long-Term Inhalation Exposure

There is potential for inhalation exposure to Sodium cyanide during sterilization and post-sterilization activities; however current exposure monitoring data are unavailable.  A study was conducted.  Rather than collecting air samples and measuring HCN concentrations in an analytical lab, a continuous monitor was used.

The current Occupational Safety and Health Administration (OSHA) permissible exposure limit (PEL) for hydrogen cyanide is 10 ppm (11 milligrams per cubic meter (mg/m3)) as an 8-hour time-weighted average (TWA) concentration.  The OSHA PEL also bears a “Skin” notation, which indicates that the cutaneous route of exposure (including mucus membranes and eyes) contributes to overall exposure.

The National Institute for Occupational Safety and Health (NIOSH) has established a recommend exposure limit (REL) for hydrogen cyanide of 4.7 ppm (5 mg/m3) as a STEL (Short term exposure limit, that level at which an unprotected worker can be exposed for 15 minutes without harm).   NIOSH also assigns a “Skin” notation to hydrogen cyanide.

A NOAEL of 65 mg HCN/m3 based on mortality in 3 of 10 rats at the LOAEL of 71 mg/m3 (HDT). Sprague-Dawley rats (15/sex/dose) were exposed to acetone cyanohydrin (ACH)[which is rapidly hydrolyzed to hydrogen cyanide at physiological pH] at concentrations of 0, 36, 101, or 204 mg ACH/m3 for 6 hours/day, 5 days/week, for 14 weeks.  Adjusted for occupational inhalation exposure, the occupational is 50 mg/m3 (46 ppm).  The exposures were equivalent to 0, 11, 32, and 65 mg HCN/m3. The NOAEL reported from the study was 204 mg ACH/m3, corresponding to 65 mg HCN/m3.  This can be estimated to correspond to a daily dose of 15 mg cyanide/kg BW/day. However, in a similar 4-week inhalation study at an average ACH concentration of 211 mg/m3 (67 mg hydrogen cyanide/m3), no systemic effects were observed, except on the first day of exposure, when the concentrations in the chamber fluctuated and reached values of 225 mg ACH/m3 (71 mg hydrogen cyanide/m3) at which dose 3 out of 10 animals died.  The dose-response relationship for cyanide is thus very steep for inhalation exposure (Dykstra, 2006).  The NOAEL/LOAEL for the inhalation endpoint is based on the acute effect of mortality for hydrogen cyanide.  The MOE is based on the uncertainty factor of 30X (3x interspecies factor and 10x intraspecies factor).  The traditional interspecies factor of 10X is reduced to 3X since the doses are expressed as air concentrations and the pharmacokinetics is assumed similar between animals and humans.  The interspecies factor of 3x is considered sufficient to account for only pharmacodynamic differences between animals and humans.

While a NOAEL of 65 mg/m3 (60 ppm) has been established, this was based on a continuous 6 hour exposure for 14 weeks.  Adjusted for occupational exposure, the inhalation exposure endpoint for hydrogen cyanide is 50 mg/m3  (46 ppm).  It is obvious from the study outlined in Appendix B that any exposure in the workplace is transient in nature and does not match the conduct of the toxicology study.  The peak 15 minute STEL from that study was 0.4 ppm (0.36 mg/m3).  Using this value results in a MOE of 115 even if is based on a very short term exposure.  It can reasonably be considered that the fumigation of citrus with NaCN offers little in the area of risk.

Cancer Risk

There is no cancer concern for this chemical.  No Q1* or MOE for cancer has been established.

Short-/Intermediate-/Long-Term Dermal Exposure and Risk

Since HCN is a gas used in outdoor environment, there is no dermal risk from the gas itself.  Potentially there could be a risk from the solid salt.  However incidence data does not support a quantified risk assessment for dermal exposure

- Risk Summary

HCN is an acute toxicant.  The very low level incidences indicate that risk from this chemical is minimal

8.0		References

1988 NIOSH PEL Project Documentation.  http://www.cdc.gov/niosh/pel88/75-56.html

American Conference of Governmental Industrial Hygienists.  TLVs and BEIs Based on the Documentation of the Threshold Limit Values for Chemical Substances and Physical Agents and Biological Exposure Indices.  Signature Publications.  2004.

EPA Reregistration Eligibility (RED) Sodium Cyanide EPA 738-R-94-020, September 1994.

Memorandum from W. Dang (OREB/HED) to J. Smith (CCB/HED) titled “Occupational and Residential Exposure Assessment and Recommendations for the Reregistration Eligibility Document for Sodium Cyanide”, dated February 28, 1994.

Email from J. Blondell (CEB/HED), dated May 3, 2005.

| Appendix A. Summary of Labels For Sodium Cyanide Products. |
| --- |
| EPA Reg No. | Use | Comments |
| 39352-50001-AA | Citrus Fumigation | Ventilation to 5 ppm, HCN gas monitors required, cloth or disposable garments and waterproof gloves are required, goggles or face shield required, two persons are required to be present, temperature not less than 60 degrees nor more than 80 degrees, restricted area of at least 20 feet around trailer, posting required, roll up doors are prohibited, 1 oz sodium cyanide per 100 ft³. |
| 35978-1 | Predator Bait | M-44 capsules, Certified Applicators only, posting required. |
| 56228-32 | Predator Bait |  |
| 39508-1 | Predator Bait |  |
| 56228-15 | Predator Bait |  |
| 1308-8 | Predator Bait |  |
| 39260-1 | Predator Bait |  |
| 35975-2 | Predator Bait |  |

## Appendix B.

| Citation Reference: | Krieger, R. (1999) "Monitoring of Personal and Work Site Air for Hydrogen Cyanide Resulting from Fumigation of Citrus": Final Draft Report. Project Number: HCN/3/99. Unpublished study prepared by University of California, Riverside. 40 p. MRID 46648901 |
| --- | --- |

## INTRODUCTION

Sodium cyanide is registered in California as Special local need (SLN CA-840006) for the generation HCN to fumigate citrus eliminate red scab another surface pests prior to shipment to Arizona.  It is used as quarantine procedure to prevent the spread of these pests.  It is used to fumigate sealed trailers, which are then aerated. These procedures are described in more detail below.

DESCRIPTION OF STUDY

The study was conducted in February and March of 1999.  Air concentrations of cyanide were measured in the breathing zone of the applicators and in the ambient air.  The trailers were treated at a rate of 1 ounce of sodium cyanide per 100 ft3 (~ 6 ounces of HCN per 1000 ft3)

Trailers are fumigated with HCN using a closed system in which the appropriate amount of sodium cyanide is mixed with concentrated sulfuric acid and water.  The trailers are fumigated for 1 hour.  They are then aerated with more than 10 air changes for ½ or 1 hour.  In February one trailer was fumigated 3 times and additional 5 trucks fumigated that same day.  In March one rig was fumigated prior to the start of monitoring.  This trailer was later fumigated and ventilated 4 more times.  In addition another trailer was fumigated and ventilated 3 times.  A total of 10 fumigation/ventilations were monitored during the study.  Each fumigation lasted for 1 hour.

Airborne HCN concentrations were measured using Safelog 100 datalogging monitor.  The monitors were zeroed using a compressed gas cylinder and calibrated using a commercially prepared 10 ppm standard of HCN in nitrogen.  The flow rate was 400 mL per minute.  One monitor was carried in the breast pocket of the fumigator.  One ambient monitor was located 50 feet from the trailer, somewhat farther than the 20 foot buffer zone required by the label.  Additional area monitors were located downwind at distances of 50, 100, and 200 feet from the trailer.  The high alarm for HCN is 10 ppm.  The high alarms for STE and TWA are each 4.7 ppm.

Following fumigation the trailers were ventilated for 1 hour through a ventilation stack with a height of 20 feet 6 inches at a rate of 800 ft3/minute.  Stack diameter was 3 inches.

The HCN levels of the personal monitor worn by the fumigator are presented in Table B1.  Exposure was low and no alarms were noted at any time.  Peak 1-minute levels were 4.7 and 5.6 for the two days.  The peak STEL was 0.4 for each of the days

| Table B1. Gas Detection Report for the Fumigator (Monitor 1) |
| --- |
| Date | Time Start-Stop | Number of Trailers | HCN Levels (ppm) |
|  |  |  | Peak (1 min) | Average | Peak STEL1 (15 min) | TWA2 |
| Feb. 18, 1999 | 10:27 am to 5:31 PM | 3 | 4.7 | 0.0 | 0.4 | 0.0 |
| Mar.3, 1999 | 9:00 am to 8:19 PM | 7 | 5.6 | 0.0 | 0.4 | 0.0 |
| The Short Term Exposure Limit (STEL) to which an unprotected worker may be exposed. The time-weighted average (TWA) is the average air concentration taken over an eight-hour period. |

The results of the ambient air monitoring are presented in Table B2.  The TWAs were all zero.  The peak 15 minute STEL ranged from 0 to 0.6.  The latter was judged to be the result of displacement of a sunshade during monitoring.

| Table B2. Ambient Air Monitoring Results |
| --- |
| Monitor No. | Month | Distance from Trailer (ft) | Peak HCN Level (1 min) | Average | Peak STEL (15 min) | TWA |
| 2 | February | 50 | 2.3 | 0.0 | 0.0 | 0.0 |
| 3 | February | 100 | 0.5 | 0.0 | 0.0 | 0.0 |
| 4 | February | 200 | 0.3 | 0.0 | 0.0 | 0.0 |
| 5 | February | 45 | 5.9 | 0.0 | 0.3 | 0.0 |
| 2 | March | 50 | 2.2 | 0.0 | 0.0 | 0.0 |
| 3 | March | 100 | 1.2 | 0.0 | 0.0 | 0.0 |
| 4 | March | 200 | 0.9 | 0.0 | 0.6 | 0.0 |
| 5 | March | 45 | 1.0 | 0.0 | 0.1 | 0.0 |