Poster Presentation 1B-14

Development and Application of an Integrated System for Ethanol Monitoring

Alhadeff, E.M., Salgado, A.M., Pereira Jr., N., Valdman*, B.

Dep. Engenharia Química

Escola de Química

Universidade Federal do Rio de Janeiro

CT- Bl E – sl 201 -Rio de Janeiro – Brasil,

Phone: (21) 2562- 7037; Fax: (21)2562-7567; E-mail: belkis@eq.ufrj.br

An automated Flow Injection Analysis system using enzymes alcohol oxidase and horseradish peroxidase was applied for quantifying ethanol reacting with 4-aminophenazone and phenol. A colorimetric detection method was developed using two different methodologies of analysis, with free and immobilized enzymes. The system with free enzymes permitted analysis of standard ethanol solution in a linear range of 0,05-1 g ethanol/l without external dilution, a sampling frequency of 15 analyses per hour, and relative standard deviation of 3,5%. A new system was designed consisting of a microreactor with 0,91 ml internal volume filled with alcohol oxidase immobilized on glass beads and addition of free peroxidase, adapted in a FIA line, for continued reuse. This integrated biosensor – FIA system is being used for quality control of biofuels, gasohol and hydrated ethanol. The FIA system integrated with the microreactor showed a logarithmic calibration curve in the range of 0.005 a 0.05 g ethanol/l and good results were obtained compared with the ethanol content measured by HPLC and CG standard methods.