Frequently Asked Questions about GOADS-2005

- How do I access the GOADS-2005 program and User’s Guide?

The program and User’s Guide can be downloaded from: http://www.gomr.mms/homepg/regulate/environ/airquality/goad.html.

They were made available at the October 13, 2004, workshop in New Orleans.

- I beta-tested the software. When I try to reinstall the program, why does the first screen asks me to modify, repair, or remove the program?

You need to select “remove” to remove the previous version of the program before installing this version.

- How can I find my MMS Company Number?

You can look up your company number at:

http://www.gomr.mms.gov/homepg/pubinfo/freeasci/freedesc.html

- How can I find my Complex and Structure ID numbers assigned by MMS?

Complex and structure IDs can be obtained from:

http://www.gomr.mms.gov/homepg/pubinfo/freeasci/freedesc.html

- Do I have to report ALL of my structures, or can some be excluded?

Living quarters can be excluded, as well as single well caissons and satellite platforms that have only fugitive emissions (i.e., no flares, dehydrators, amine units, fired vessels or internal combustion engines). Platforms, as above, with a minimal (5 or less) amount of small gas driven pumps/bleeding controllers and single cranes that run intermittently (avg. 1 hr. per week) can also be excluded.  Also, platforms with fugitives and a diesel crane that operate intermittently (e.g., average usage less than 30 hours per month) are excluded.

- What are the similarities between GOADS-2000 and GOADS-2005?

MMS is requesting that you track monthly activities for variables needed to calculate emissions, and provide the data in one annual submittal.

The same emission sources are covered:

Amine units

Boilers/heaters/burners

Diesel and gasoline engines

Drilling rigs

Combustion flares

Fugitive sources

Glycol dehydrators

Loading operations

Losses from flashing

Mud degassing

Natural gas engines

Natural gas turbines

Pneumatic pumps

Pressure/level controllers

Storage tanks

Cold vents

The program performs the same type of QC checks when the monthly data are saved.

The same QA Summary Form is to be printed out and submitted to MMS with the annual submittal.

- What are the differences between GOADS-2000 and GOADS-2005?

The program now has a print screen function.

The program now has an export to spreadsheet function.

The platform and equipment data only need to be entered once for a number of parameters such as block, area, name, latitude/longitude, fuel type, and stack parameters.  The cut and paste feature has been removed.

The speed of the program has been greatly enhanced.

GOADS-2005 now has an import/export feature that can be used when platform ownership changes during 2005.

Improvements have been made to some confusing screens (cold vents and combustion flares).

“No Emissions to Report” is used instead of status and effective date.  When you select “No Emissions to Report” for any given month for an entire structure or individual pieces of equipment, it means there was NO activity for that month, and MMS should not apply surrogate data to calculate emission estimates.

Note that if the user selects " No Emissions to Report,” then all activity data that might have been previously entered will be ignored for calculation of emissions.

Only platform and equipment data that change monthly need to be entered for each month.

Platform data that need to be entered for every month:

1- Total fuel used

2- Oil and gas produced

3- Oil and gas throughput

Monthly Equipment Activity Data Required

| Equipment Type | Monthly Activity Data |
| --- | --- |
| Amine units | Hours operated Processed throughput |
| Boilers/heaters/burners | Average heat input Hours operated Average fuel usage Total fuel used |
| Diesel and gasoline engines | Operating horsepower Hours operated Average fuel usage Total fuel used |
| Drilling operations | Hours operated Total diesel fuel usage Total gasoline fuel usage Total natural gas fuel usage |
| Combustion flares | Hours operated Total volume flared including upsets |
| Glycol dehydrators | Hours operated Processed throughput Glycol circulation rate |
| Loading operations | Bulk liquid temperature Volume loaded |
| Losses from flashing | Operating pressure upstream of vessel Operating temperature upstream of vessel Operating pressure of vessel Operating temperature of vessel Oil/condensate throughput SCF of flash/barrel |
| Mud degassing | Days per month drilling with mud |
| Natural gas engines | Operating horsepower Hours operated Average fuel usage Total fuel used |
| Natural gas turbines | Operating horsepower Hours operated Average fuel usage Total fuel used |
| Pneumatic pumps | Hours operated Fuel usage rate |
| Pressure/level controllers | Hours operated Fuel usage rate |
| Storage tanks | Average liquid height Bulk liquid temperature API gravity Reid vapor pressure Product throughput Average mole weight of VOC Average % by weight of VOC |
| Cold vents | Vent gas VOC concentration Hours operated including upsets Volume vented including upsets Vent gas H2S concentration Average mole weight of VOC |

- How do I navigate between being able to add and edit activity data and descriptive data?

The  Edit Activity Data   and In   Edit Description Data   buttons on the lower left side of the screen transfer you from one data edit mode to the other.  If you are editing the monthly activity data, you will see the descriptive data but not be able to revise them.

9.	Is there any way I can re-use the GOADS-2000 data files for this 2005 inventory effort?

GOADS-2005 has a file import feature for your 2000 data files.  You need to obtain your 2000 files from MMS, however, because the GOADS-2005 program structure is different.  After importing the data files, you need to create records for new structures and equipment that were not in place in 2000.  You also need to closely review and edit the imported 2000 data to make sure they reflect operations for 2005.

- GOADS-2005 lets me enter only one MMS Company ID.  How do I use the program to enter and submit data for more than one company?

GOADS-2005 was designed as a single-user, stand-alone software program for use by a single company.  However, it can be installed onto different PCs to enter data for different companies.

Additionally, there is a work-around to enter data for multiple companies:

1. Install the GOADS-2005 software.

2. Before running the program, open the Windows folder C:/Program Files/ and copy and paste the entire folder named GOADS-2005 into the Program Files folder to create an additional installation folder. Rename the new folder with a name that represents the company.  You may create as many installation folders as you like.

3. Each folder will contain a separate program file (GOADS-2005.exe) and database (GOADS.mdb). Create a link to each separate program file and place it on your Windows desktop for convenient access.  Rename the link to indicate the company it represents. Each separate link will create a separate company-specific GOADS-2005 database when run for the first time.

4. When you run each company-specific GOADS-2005 program file from Windows Explorer directly or from the desktop link, it will prompt you for the MMS Company ID and store the information in the GOADS.mdb in that same directory.  All data entered and reported will be specific to that installation folder.

The Start Menu icons will start only the original installed program file in C:/Program Files/GOADS-2005/.

11.	 Does MMS have any guidance on how to populate the cold vent screen?

To begin with, for equipment that is vented remotely to a cold vent, create the cold vent record FIRST. If a vent ID is not entered, the program will automatically assume the equipment is vented locally.

Note that vented emissions are NOT combusted.  If emissions are combusted, create a Combustion Flare record.

It is important to make sure that your monthly volume vented and flared total are consistent with your monthly OGOR-reported value.  MMS will review both data submittals for consistency.

12.	Does MMS have any guidance on how to populate the combustion flare    screen?

To begin with, for equipment that is flared remotely, create the flare record FIRST. If a flare ID is not entered, the program will automatically assume the equipment is flared locally.

Note that flared emissions are combusted.  If emissions are not combusted, create a Cold Vent record.

It is important to make sure that your monthly volume vented and flared total are consistent with your monthly OGOR-reported value.  MMS will review both data submittals for consistency.

- Does MMS have any guidance on how to populate the losses from the flashing screen?

The preferred data for this screen are to supply data for "SCF of flash per bbl of oil" along with the "Type of vessel," "API gravity of stored oil" and the "Oil/Condensate throughput."  No data are needed for the operating pressures and temperatures of the vessels if these data are supplied in GOADS.

An operator can obtain these data using the following methods:

  - Direct measurement

  - Vasquez-Beggs Correlation Equations (SPE Paper 6719)

www.nmenv.state.nm.us/aqb/Vasquez-Beggs-Flashing-Calculations.xls.

  - Griswold and Ambler GOR Chart Method (SPE Paper 7175)

http://www.epa.gov/gasstar/pdf/lessons/ll_final_vap.pdf

  - Pressurized oil sample and measurement of gas-to-oil ratio (GOR) in lab

  - American Petroleum Institute's (API) E&P TANK Version 2 software

  - Process simulators such as HYSYS or PROSIM

Flash gas is natural gas liberated when crude oil and condensate undergo a pressure drop.  There are many areas in the production, gas processing and transmission processes where flash gas is generated and vented to the atmosphere, including:

- Intermediate Flash:  high/intermediate-pressure separators that send crude oil and condensate to a low-pressure separator.  This low-pressure separator operates at a pressure greater than atmospheric pressure and may vent directly to the atmosphere.  A heater treater may also be utilized in an intermediate flash situation.  (See diagram below.)

- Fixed Roof Storage Tanks:  high/low-pressure crude oil and condensate are flashed into tanks operating at atmospheric pressure. (See diagram below.)

Note that for storage tanks, emissions from flashing are in addition to working and breathing emissions.

Below is a diagram of possible flash losses and routes for the flash gas.

For each stage of flash (e.g., low-pressure separator oil to heater treater) that is vented to the atmosphere (locally or to remote vent) or flared (locally or to remote flare), the operator should give the following data:

- Type of vessel (high-pressure separator, low-pressure separator, heater treater, surge tank, storage tank).

- API gravity of stored oil

- Operating pressure of vessel that has flash gas that is vented or flared

- Operating temperature of vessel that has flash gas that is vented or flared.

- Oil/Condensate throughput

- Operating pressure of vessel upstream of vessel with flash gas that is vented or flared

- Operating temperature of vessel upstream of vessel with flash gas that is vented or flared.

- If available, the "SCF of flash per bbl of oil" can be entered along with the "Type of vessel," "API gravity of the stored oil" and "Oil/Condensate Throughput."  If the "SCF of flash per bbl of oil" is entered, then the company does not have to enter the operating pressures and temperatures of the vessels.

For example, an operator has a low-pressure separator (LP) that sends its oil to a heater treater (HT), which dumps its oil to an atmospheric storage tank (T-1) that vents its flash gas to the atmosphere locally.  The low-pressure separator sends its flash gas to the suction of the onsite compressor (i.e., the system).  The heater treater vents its flash gas remotely to the low-pressure vent system.  The operator would create two flash records, say FLASH-1 and FLASH-2.  On FLASH-1, enter data for the flash between the LP to HT flash, and on FLASH-2, enter data for the flash between the HT and T-1 flash.  Since the LP separator sends its gas to the onsite compressor, this flash is not vented to the atmosphere (or flared) and would not be reported.

- Does MMS have any guidance on how to populate the fuel combustion screens?

Diesel average heating value:  average = 19,300 Btu/lb

Natural gas average heating value = 1,050 Btu/scf

Gasoline average heating value = 20,300 Btu/lb

To calculate total fuel used, see equations in the User’s Guide (and help screens) for diesel and gasoline engines, boilers/heaters/burners, natural gas engines, and natural gas turbines.

- Sometimes the requested data are grayed out and I cannot edit them.  Why is this?

GOADS-2005 will not let you see data that you have entered that are in conflict with other data and selections you have made.  For example, if you indicate that a piece of equipment is vented locally and enter details on the local vent, the program will save the information.  If you then change the equipment to be vented remotely (where details on the remote vent are recorded on the cold vent screen instead), the local vent data will be “grayed out” so you know that MMS will ignore the local vent data and use the remote vent information instead of the local vent information.

16.	Does MMS have any guidance on how to populate the fugitives screen?

The following information is from the User’s Guide and help screen:  Average VOC weight percent of fugitives – The average VOC content of fugitive emissions for the inventoried components and the selected stream type. You may find it beneficial to use the following information as a starting point.

Speciation Fractions for Total Hydrocarbon (THC) Emissions By Stream Type

| THC Fraction | Gas | Light Oil (( 20 API Gravity) | Heavy Oil ((20 API Gravity) | Water/Oil* |
| --- | --- | --- | --- | --- |
| Methane | 0.945 | 0.612 | 0.942 | 0.612 |
| Volatile Organic Compounds (VOC) | 0.0137 | 0.296 | 0.030 | 0.296 |

Source:  API, 1996.  Calculation Workbook for Oil and Gas Production Equipment Fugitive Emissions.

The following information provided by the Offshore Operators Committee may also be helpful in compiling a component count:

Summary of Equipment Inventory Data (Number of Components) by Skid Type

| Skid Type | Valves | Pump Seals | Threaded Connections | Flanges | Open Ended Lines | Compressor Seals* | Diaphragms | Drains | Dump Arms | Hatches | Instruments | Meters | Pressure Relief Valves | Polished Rods | Other Relief Valves |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Separator Skid | 34 | 0 | 13 | 73 | 0 | 0 | 0 | 2 | 0 | 0 | 15 | 1 | 1 | 0 | 0 |
| Heater Treater Skid | 98 | 0 | 70 | 114 | 0 | 0 | 0 | 3 | 0 | 0 | 25 | 0 | 3 | 0 | 0 |
| LACT Charge Pump Skid | 21 | 3 | 6 | 47 | 0 | 0 | 0 | 1 | 0 | 0 | 9 | 0 | 0 | 0 | 0 |
| LACT Skid | 62 | 1 | 75 | 69 | 0 | 0 | 0 | 1 | 0 | 0 | 34 | 4 | 6 | 0 | 0 |
| Pipeline Pumps Skid | 39 | 3 | 12 | 78 | 0 | 0 | 0 | 2 | 0 | 0 | 70 | 0 | 3 | 0 | 0 |
| Pig Launcher/Receiver Skid | 13 | 0 | 14 | 16 | 0 | 0 | 0 | 0 | 0 | 0 | 9 | 0 | 1 | 0 | 0 |
| Compressor Skid | 119 | 0 | 113 | 138 | 0 | 4 | 0 | 1 | 0 | 0 | 69 | 0 | 9 | 4 | 0 |
| Filter/Separator Skid | 30 | 0 | 25 | 37 | 0 | 0 | 0 | 1 | 0 | 0 | 9 | 0 | 1 | 0 | 0 |
| Gas Dehydration Skid | 23 | 0 | 14 | 40 | 0 | 0 | 0 | 1 | 0 | 0 | 12 | 0 | 1 | 0 | 0 |
| Glycol Regeneration Skid | 134 | 0 | 110 | 194 | 0 | 0 | 0 | 4 | 0 | 0 | 45 | 1 | 7 | 6 | 1 |
| Gas Meter | 10 | 0 | 11 | 26 | 0 | 0 | 0 | 1 | 0 | 0 | 21 | 2 | 0 | 0 | 0 |
| Fuel Gas Skid | 62 | 0 | 47 | 85 | 0 | 0 | 0 | 1 | 0 | 0 | 32 | 1 | 4 | 0 | 0 |
| Flotation Cell Skid | 41 | 1 | 34 | 70 | 0 | 0 | 1 | 1 | 0 | 15 | 8 | 0 | 2 | 0 | 2 |
| Scrubber | 13 | 0 | 13 | 18 | 0 | 0 | 0 | 1 | 0 | 0 | 9 | 0 | 1 | 0 | 0 |
| Amine Unit | 226 | 8 | 166 | 391 | 0 | 0 | 1 | 5 | 0 | 0 | 121 | 2 | 12 | 0 | 1 |
| Line Heater | 30 | 0 | 46 | 18 | 0 | 0 | 0 | 1 | 0 | 0 | 10 | 0 | 0 | 0 | 1 |
| Production Manifold | 108 | 0 | 31 | 148 | 0 | 0 | 0 | 1 | 0 | 0 | 43 | 0 | 0 | 7 | 0 |
| Wellhead | 15 | 0 | 6 | 19 | 0 | 0 | 0 | 0 | 0 | 0 | 11 | 0 | 0 | 0 | 0 |
| Import or Export Pipeline | 3 | 0 | 0 | 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

17.  Where can I get information on reducing venting and flaring emissions?

The Natural Gas STAR Program is a flexible, voluntary partnership between EPA and the oil and natural gas industry. Through the Program, EPA works with companies that produce, process, and transmit and distribute natural gas to identify and promote the implementation of cost-effective technologies and practices to reduce emissions of methane, a potent greenhouse gas.  For more information see www.epa.gov/gasstar.

18. What is the average H2S content of pipeline quality gas?

For sweet pipeline quality gas, use 4 ppm H2S.

Pipeline quality specifications are usually 0.25 grains H2S per 100 SCF.  One grain of H2S per 100 SCF is equal to 16 ppm.

19.  What are standard conditions?

Standard pressure of 14.7 psia and standard temperature of 60°F.

20.  When do I have to report drilling?

You must report drilling activities for GOADS 2005 for all:

- Platform Rig applications

- Any Jack-up rig associated with an Area/Block with existing production structures.

21.  How do I allocate fuel to different equipment?

Most platforms meter only total fuel (Natural Gas, Diesel or Gasoline) used.  To allocate fuel to each piece of fuel burning equipment do the following:

- Calculate the theoretical fuel used for each piece of equipment based on the fuel efficiency and hours operated for the month, e.g. btu/hp-hr for engines or MMbtu/hr for heater treaters.

- To Calculate Theoretical Fuel Use for Natural Gas Engine, use the following formula.

SCF/Month= (Hrs/Month) (hp) (btu/hp-hr) (scf/1050 btu)

- To Calculate Theoretical Fuel use for Heater/Treater or Burner, use the following formula.

SCF/Month= (Hrs/Month) (MMbtu/hr) (scf/1050 btu) (1,000,000 btu/MMbtu)

- To Calculate Theoretical Fuel Use for Diesel Engine, use the following formula.

Gals/Month= (Hrs/Month) (hp) (btu/hp-hr) (1lb/19,300 btu) (1 gal/7.2558lb)

22.  What are the surrogate data for?

The surrogate data are for use as default data.  If you do not have and cannot get information about a piece of equipment or scientific data, use the surrogate data.  MMS has approved these data for your use.  (See table below.)

Surrogate Stack Parameters Used to Supplement GOADS Data.

| Unit | Field | Default Value |
| --- | --- | --- |
| Amine Unit | Elevation (above sea level) | 50 ft |
| Amine Unit– ventilation system for acid gas from reboiler | Exit velocity (ft/sec) | Calculated with AMINECalca |
| Amine Unit– ventilation system for acid gas from reboiler | Exit temperature | 110 oF |
| Amine Unit–ventilation system for acid gas from reboiler | Combustion temperature | 1832 oF |
| Boiler/heater/burner | Elevation (above sea level) | 50 ft |
| Boiler/heater/burner – exhaust System | Exit temperature | 400 oF |
| Boiler/heater/burner – exhaust system | Outlet orientation | 0 degrees |
| Boiler/heater/burner – exhaust system | Outlet diameter | 12 inches |
| Boiler/heater/burner – exhaust system | Exit velocity | Calculated |
| Diesel Engine | Elevation (above sea level) | 50 ft |
| Diesel Engine | Max rated fuel use | 7000 Btu/hp-hr |
| Diesel Engine | Avg fuel use | 7000 Btu/hp-hr |
| Diesel Engine– exhaust system | Outlet height | 7 ft above engine |
| Diesel Engine– exhaust system | Exit velocity | Calculated |
| Diesel Engine– exhaust system | Exit temperature | 900 oF |
| Diesel Engine– exhaust system | Outlet orientation | 0 degrees |
| Diesel Engine– exhaust system | Outlet diameter | 12 inches |
| Flare | Combustion temperature (excluding upsets) | 1832 oF |
| Flare | Stack orientation | 0 degrees |
| Flare | Outlet diameter | 12 inches |
| Glycol Dehydrator | Elevation (above sea level) | 50 ft |
| Glycol Dehydrator– flash tank | Temperature | 120 oF |
| Glycol Dehydrator– flash tank | Pressure | 60 psig |
| Glycol Dehydrator– ventilation system | Exit temperature | GLYCalc default (usually 212 oF)b |

| Surrogate Stack Parameters Used to Supplement GOADS Data (Continued). |
| --- |
| Unit | Field | Default Value |
| Glycol Dehydrator– ventilation system | Outlet orientation | 0 degrees |
| Glycol Dehydrator– ventilation system | Flare feed rate (scf/hr) | Calculated with GLYCalcb |
| Glycol Dehydrator– ventilation system | Combustion temperature | 1832 oF |
| Glycol Dehydrator– ventilation system | Condenser temperature | 110 oF (or calculated with GLYCalc)b |
| Glycol Dehydrator– ventilation system | Condenser pressure | 14.8 psia |
| Loading – barge | Elevation (above see level) | 0 |
| Loading – ventilation system | Exit temperature | 70 oF |
| Loading– ventilation system | Outlet orientation | 0 degrees |
| Loading– ventilation system | Outlet diameter | 3 in. |
| Loading– ventilation system | Exit velocity | Calculated |
| Loading– ventilation system | Flare feed rate | Calculated (use loading exhaust vol. flow rate if controlled by flare) |
| Loading– ventilation system | Combustion temperature | 1832 oF |
| Losses from Flashing– ventilation system | Exhaust volume flow rate | Calculated |
| Losses from Flashing– ventilation system | Exit velocity | Calculated |
| Losses from Flashing– ventilation system | Exit temperature | 70 oF |
| Losses from Flashing– ventilation system | Outlet diameter | Use Tank Vent Outlet Diameter |
| Natural Gas Engine | Max rated fuel usage | 7000 Btu/hp-hr |
| Natural Gas Engine | Avg fuel usage | 7000 Btu/hp-hr |
| Natural Gas Engine– exhaust system | Exit velocity | Calculated |
| Natural Gas Engine– exhaust system | Exit temperature | 4-cycle rich burn: 1100 oF |
| Natural Gas Engine– exhaust system | Exit temperature | 2-cycle lean burn: 700 oF |
| Natural Gas Engine– exhaust system | Outlet diameter | 12 inches |
| Natural Gas Turbine | Max rated fuel use | 10,000 Btu/hp-hr |
| Natural Gas Turbine | Avg fuel use | 10,000 Btu/hp-hr |
| Natural Gas Turbine– exhaust system | Exit velocity | Calculated |
| Natural Gas Turbine– exhaust system | Outlet diameter | 12 inches |
| Natural Gas Turbine– exhaust system | Exit temperature | 1000 oF |
| Pneumatic Pumps | Elevation (above sea level) | 50 ft |
| Pneumatic Pumps– ventilation system | Exit velocity | Calculated |
| Pneumatic Pumps– ventilation system | Exit temperature | 70 oF |
| Pressure/level Controllers | Elevation (above sea level) | 50 ft |
| Storage tank – General Information | Roof Height above Shell (ft) | 0.0625*(Tank Diameter, ft / 2) |
| Storage tank– ventilation system | Exit velocity | Calculated |
| Storage tank– ventilation system | Exit temperature | 70 oF |
| Storage tank– ventilation system | Outlet orientation | 0 degrees |
| Storage tank– ventilation system | Flare feed rate | Calculated (or use the calculated storage tank exhaust vol. flow rate) |
| Vent | Outlet elevation (above sea level) | 50 ft |
| Vent | Outlet diameter | Calculated (average of submitted data) |
| Vent | Exit temperature | 70 oF |
| Vent | Outlet orientation | 0 degrees |
| Vent– upsets | Exit temperature | 70 oF |

a  AMINECalc is released by the Gas Technology Institute as part of the AIRCalc Air Emissions Inventory Report Management Software Program (GTI 2001)

b  GLYCalc is released by the Gas Technology Institute, formerly the Gas Research Institute (GRI) (GTI 2000)

23.  How do I convert API Gravity to Specific Gravity?

Specific gravity of oil = 141.5/(API gravity + 131.5)

24. What are the Ideal Gas Law Relationships?

Standard Conditions are 14.7 psia and 60 o F or 520 o R.  Note: o R= degrees Rankine =( o F + 460)

1 lb-mole of gas occupies approximately 379 standard cubic feet.

25. How do I calculate the weight in lbs of a gas that has a molecular weight of 18 lbs/lb-mole?

Lbs of gas = (SCF)(1 lb-mole/379 SCF)(18 lbs gas/lb-mole)

- How do I calculate horsepower of a compressor?

Horsepower of Compressor from Discharge, Suction Pressure and Compressed Gas Volume

Hp = [50.5 * (1.255 / (1.255 - 1)) * (((Discharge Pressure + 14.7) / (Suction Pressure + 14.7)) ^ 0.203) – 1) * MMSCFD] + 5% total hp for externally driven equipment

- How do I calculate Exit Velocity for Boiler/heater/burner, ft/sec?

- How do I calculate Exit Velocity for Diesel Fired Engine, ft/sec?

- How do I calculate Exit Velocity for Flare, ft/sec?

- How do I calculate Loading Exhaust Vol. Flow Rate, SCF/hr?

31.  How do I calculate Flashing Exhaust Vol. Flow Rate, SCF/hr?

32.  How do I calculate Vent Exhaust Vol. Flow Rate, SCF/hr?

- How do I calculate Exit Velocity (applicable for Flashing Losses, Glycol Dehydrators, Pneumatic Pumps, Loading, Storage Tanks, and Vents), ft/sec?

- How do I calculate Exit Velocity for Rich-burn, Natural Gas Fired Engine, ft/sec?

35.	How do I calculate Exit Velocity for Lean-burn, Natural Gas Fired Engine, ft/sec?

36.  How do I calculate turbine exit velocity?