MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A17359 | In-Flight Anomaly Number -- | Contractor Report Number P-087 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title PROPULSION - HELIUM INJECT LINE LEAKAGE AT B-NUT TO UNION |
| EICN# -- | ELEMENT ET | Contractor LMMSS | FSCM# 06887 | FCRIT 1R |
| HCRIT -- | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE ET COMPLETE | PART# 11931-009 AND -019 | SER/LOT# ET-102 | MANUFACTURER LMMSS |
| Test/Operation AS - ATS | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode MV - EXT LEAK | Cause MA - MFG-ASY |
| System PROPULSION | Defect -- | Material -- | Work Contact E. ALDAHIR | Fail Date 01/12/1999 |
| Received at MSFC 01/13/1999 | Date Isolated 01/12/1999 | FMEA Reference 2.4.10.1 & 2.4.11.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom MV - EXT LEAK | Time Cycle -- |
| Effectivity Text ET 102 |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 04/29/1999 | Contractor Req Defer Until Date 01/12/1999 | LVL 3 Close -- | Remark / Action 02/01/1999 |
| Investigation / Resolution Summary |
| Last MSFC Update 03/01/1999 | CN RSLV SBMT -- | Defer Date -- | Add Date 01/13/1999 | R/C Codes -- -- -- |
| Assignee |
| Design M. BUTLER | Chief Engineer J. LUSK | S & MA S. GORUM | Project -- | Project MGR P. COUNTS |
| Approval |
| Design M. BUTLER | Chief Engineer J. LUSK | S & MA S. GORUM | Project -- | Project MGR P. COUNTS |
| PAC Assignee R. TUCKER | PAC Review Complete RT | MSFC Closure Date 02/25/1999 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID N037551 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description PROBLEM A PROBLEM OCCURRED ON ET-102 IN BLDG. 420 DURING LEAK CHECK PROCEDURE TP-8C101-AT. JOINTS 32 AND 33 ON THE HELIUM INJECT LINE FAILED "BUBBLE" LEAK CHECK AT THE B-NUT UNION FITTING TM04K REQUIRES THAT THERE BE "NO DETECTABLE BUBBLES" WHEN THE SYSTEM IS PRESSURIZED TO 750 +/- 50 PSIG, GHE AND LEAK DETECTION SOLUTION IS APPLIED ON THE B-NUT JOINTS CRITICALITY: THE LINES ARE CRIT. 1R; FMEA ITEM CODE: 2.4.10.1 & 2.4.11.1; LEAKAGE * REVISION "A" DATED 2-1-99 - UPDATES AND CLOSES ALL TASKS SEE ASTERISKS |
| Contractor Investigation/Resolution GENERAL THE HE INJECT LINE TRANSPORTS GROUND GHE TO SUPPLY A CONTROLLED FLOW OF HELIUM INTO THE AFT ELBOW OF THE LO2 FEEDLINE WHICH PROVIDES PROPELLANT CONDITIONING AND PREVENTS GEYSERING. THE LINE CONSISTS OF FLARED TUBES AND UNIONS JOINED WITH B-NUTS THE FLARED TUBES ARE FABRICATED FROM 321 CRES, THE UNIONS (MS 24392-J6) 304 CRES. THE JOINT IS ASSEMBLED WITH A COPPER CRUSH WASHER PLACED OVER THE CONICAL END OF THE UNION WITH THE FLARED TUBE END THEN CENTERED OVER THIS UNION/CRUSH WASHER COMBINATION. THIS ASSEMBLY IS SECURED WITH A B-NUT TORQUED TO 270-300 INCH POUNDS BOTH LINES SHOWED LEAKAGE AT INITIAL TESTING. AFTER REPLACEMENT OF THE CRUSH WASHERS AT JOINTS 32 AND 33, AND TORQUEING TO THE MAXIMUM TORQUE ALLOWABLE, THE JOINTS FAILED BUBBLE LEAK CHECK. THE UNION AND CRUSH WASHERS HAVE BEEN REMOVED AND REPLACED AS PER NCD N037551 (REFERENCE: IPRAS 794960) AND PASSED TESTING PER TP-8C101-AT TASK I. FAILURE INVESTIGATION A PERFORM INVESTIGATION TO DETERMINE CAUSE OF LEAKAGE. THIS WILL INCLUDE DIMENSIONAL INSPECTION, VISUAL INSPECTION, NCD REVIEW, AND METALLURGICAL ANALYSIS RESPONSIBILITY: E. ALDAHIR & W. MATTHEESSEN/3741 D. WESTPHAL/3740 ECD: 01/29/1999 COMPLETE: 1/19/1999 * CLOSURE STATEMENT: * 1) A SCHEMATIC OF THE MS24392-J6 UNION FITTING IS ILLUSTRATED IN FIGURE I (IN CONTRACTOR'S ORIGINAL HARDCOPY) * 2) THE RESULTS OF THE DIMENSIONAL INSPECTIONS ARE SHOWN IN TABLE I TABLE I.MS24385 STANDARD DIMENSIONAL VALUES VERSUS ACTUAL (MS24392-J6) WEBER AEROSPACE UNION FITTING DIMENSIONAL VALUES. (NOTE: MS24385 SUPERSEDES MS24392) ******************************************************************** *ITEM * ID" * MD" * MID" * PD" *CS * L" * J" * H * ******************************************************************** *MS24385*0.297 * 0.5538- *0.4916- *0.5230- *37 *1.375 *0.556 *0.005* * +/- 0.004 * 0.5625 *0.4983 *0.5264 *1/2*.0156 *0.015 * MAX.* * * * * ACTUAL *1.374 *0.561 *0.002* * IN FLOW END ***************************************************** *ACTUAL (0.291-* 0.5573 *0.4933 *(0.5227)*37 DEGREES * * 0.293)* * * * * * OUT FLOW END* * * * * *ACTUAL (0.280-* 0.5594 *0.4937 *0.5249 *(38 DEGREES) * * 0.285)* * * * * ******************************************************************** ID=INNER DIAMETER, MD=MAJOR DIAMETER, PD=PITCH DIAMETER, L=TOTAL LENGTH, CS=CONICAL SURFACE, J=REF. MS24358 H=PERPENDICULARITY FLOW PLANE TO HEX SIDE NOTE: NUMBERS IN PARATHESISES IN TABLE I DENOTE OUT OF TOLERANCE DIMENSIONS FOR THE SUSPECT MS24392-J6 UNION FITTING AFTER IT WAS INSTALLED AND REMOVED. THE UNION FITTING'S OUT OF TOLERANCE DIMENSIONS ARE AS EXPECTED, DUE TO ITS REMOVAL AND INSTALLATION * 3) ON JANUARY 18, 1999 THE SUSPECT MS24392-J6 UNION FITTING WAS CHECKED FOR LEAKS BY PRESSURIZING THE UNION FITTING AND SUBMERGING IT IN WATER. THE IN FLOW END OF THE UNION FITTING DISPLAYED AN OBVIOUS VIGOROUS LEAK WITH ONLY 5 PSI OF PRESSURE APPLIED TO THE FITTING * 4) THE VISUAL INSPECTION AND THE PHOTOGRAPHIC INSPECTION OF THE SUSPECT MS24392-J6 WEBER AEROSPACE UNION FITTING RESULTED IN THE FOLLOWING: A) THE THREADS ON THE IN FLOW END OF THE FITTING ARE NOT PROPERLY THREADED (I.E. INCOMPLETE THREADING) B) THE CONICAL SECTION OF THE OUT FLOW END OF THE UNION FITTING IS CONCAVE IN SHAPE, WHICH IS A NORMAL DEFORMATION AFTER INSTALLATION. THE CONICAL SECTION OF THE IN FLOW END OF THE UNION FITTING EXHIBITED EVIDENCE OF NO CONTACT WITH THE MATING TUBE, SINCE THERE WAS NO DEFORMATION ON THE CONICAL SECTION OF THE FITTING C) THE UNION FITTING HAS OBVIOUS NICKS AND SCRATCHES ON THE WHOLE PART * 5) THE CHEMICAL ID AND THE HARDNESS CHECK OF THE SUSPECT MS24392-J6 WEBER AEROSPACE UNION FITTING RESULTED IN THE FOLLOWING: A) THE CHEMICAL ID REVEALED THAT THE UNION FITTING IS A 304 CRES, WHICH MEETS THE MS24385 STANDARD REQUIREMENT B) THE HARDNESS CHECK IS EQUAL TO AN AVERAGE VALUE OF 24.1 HRC, WHICH IS TO BE EXPECTED FOR 304 MATERIAL * 6) THE NCD HISTORY REVIEW DISCOVERED ONLY THE FOLLOWING NCDS: A) T094991 WAS INITIATED ON 3/12/1987 FOR 1925 UNION FITTINGS, OF WHICH 600 WERE MS24392-J6, THAT WERE FOUND TO HAVE NICKS. THE SUSPECT UNION FITTINGS WERE IN VIOLATION OF THE MS24385 STANDARD REQUIREMENTS T094991 WAS DISPOSITIONED BY MRB AS USE AS IS B) N037551 WAS DUE TO THE UNION FITTING IN QUESTION * 7) A VISUAL INSPECTION THROUGH CLEAN BAGS WAS CONDUCTED ON 30 MS24392-J6 WEBER AEROSPACE UNION FITTINGS. THE 30 UNION FITTINGS EXHIBITED NICKS AND SCRATCHES THAT WERE VISIBLE TO THE NAKED EYE. (NOTE: THE 30 TRACEABLE UNION FITTINGS WERE FOUND TO BE THE ONES, WHICH WERE PREVIOUSLY ACCEPTED ON T094991.) * SUMMARY OF TASK 1.A: THE CAUSE OF THE LEAK WAS ISOLATED TO THE INCOMPLETE THREADING PROCESS ON THE IN FLOW END OF THE WEBER AEROSPACE UNION FITTING. THE INCOMPLETE THREAD PREVENTED THE FLARED TUBE END TO COMPLETELY SEAT ON THE CONICAL SURFACE OF THE UNION FITTING DURING TORQUE APPLICATION * B BASED ON THE FAILURE CAUSE, A 100% STOCK CHECK OF MS24392-J6 UNION FITTINGS (WEBER AEROSPACE AND ASC) IN STORES IS TO BE CONDUCTED. RECEIVING INSPECTION IS TO INSPECT THE UNION FITTINGS BY WAY OF VISUAL INSPECTION METHOD TO CHECK FOR PROPER THREADING RESPONSIBILITY: F. WILLIAMS/3762 - S. PARIKH/3760 ECD: 01/29/1999 COMPLETE: 1/26/1999 * CLOSURE STATEMENT: ALL OF THE 321 MS24392-J6 UNION FITTINGS (WEBER AEROSPACE AND ASC) IN STORES WERE VISUALLY INSPECTED, 320 OF THEM WERE ACCEPTED AND ONE WAS REJECTED DUE TO PART NOT BEING DEBURRED ON ONE END OF THE UNION FITTING. RELIABILITY ASSURANCE HAS CONFIRMED RECEIVING INSPECTIONS FINDING (REF. N039784) BASED ON THE INSPECTION OF THE 321 PARTS, FURTHER INSPECTION OF SIMILAR UNION FITTINGS FOR THIS ISOLATED ANOMALY IS NOT WARRANTED. IN ADDITION, NO SCAR ACTION IS JUSTIFIED FOR THE SUPPLIER (WEBER AEROSPACE) * C. RECEIVING INSPECTION (DEPT. 3762) WILL ADDRESS VIA CREW THE ANOMALY FOUND IN PARAGRAPH I.A.4.A. FOR FUTURE VISUAL INSPECTION OF MS24XXX UNION FITTINGS RESPONSIBILITY: F. WILLIAMS/3762 - S. PARIKH/3760 ECD: 02/5/1999 COMPLETE: 02/01/1999 * CLOSURE STATEMENT: AS AN ENHANCEMENT, THE RECEIVING INSPECTION SUPERVISOR (DEPT. 3762) HELD A CREW MEETING TO ADDRESS THE MISTHREADED UNION FITTING ANOMALY IN ORDER TO HEIGHTEN EMPLOYEE AWARENESS. (REF. ATTACHED CC MAIL FROM F. WILLIAMS) TASK CLOSED * CAUSE: THE CAUSE OF THE LEAK WAS ISOLATED TO AN INCOMPLETE THREADING PROCESS ON THE IN FLOW END OF THE UNION FITTING. THE INCOMPLETE THREAD PREVENTED THE FLARED TUBE END TO COMPLETELY SEAT ON THE CONICAL SURFACE OF THE FITTING DURING TORQUE APPLICATION * TASK II. CORRECTIVE ACTION BASED ON NONCONFORMANCE HISTORY AND STOCK INSPECTION, THIS IS AN ISOLATED INCIDENT ATTRIBUTED TO NORMAL PRODUCTION FALL-OUT. AS AN ENHANCEMENT A RECEIVING INSPECTION CREW MEETING WAS HELD TO MAKE THEIR DEPARTMENTAL EMPLOYEES AWARE OF THE ANOMALY TASK CLOSED * TASK III. CLEARANCE OF EFFECTIVITIES ALL ETS CLEARED THE PURPOSE OF LEAK TESTING IS TO FILTER OUT SUCH DISCREPANCIES. ALL INSTALLED JOINTS PASSED TP-8C101-AT LEAK TESTING TASK CLOSED * TASK IV. CAPS CLOSURE SUMMARY A PROBLEM OCCURRED DURING LEAK CHECK ON ET-102 IN BLDG 420 DURING PERFORMANCE OF LEAK CHECK PROCEDURE (TP-8C101-AT). TWO JOINTS (32 AND 33) ON THE HELIUM INJECT LINE FAILED "BUBBLE" LEAK CHECK. THE TM04K REQUIREMENT IS "NO DETECTABLE BUBBLES" WHEN THE SYSTEM IS PRESSURIZED TO 750 +/- 50 PSIG, GHE AND LEAK DETECTION SOLUTION IS APPLIED ON THE B-NUT JOINTS THE INVESTIGATION REVEALED THAT THE ROOT CAUSE OF THE LEAK WAS ISOLATED TO THE INCOMPLETE THREAD ON THE IN FLOW END OF THE FITTING. THE INCOMPLETE THREAD NEVER ALLOWED THE FLARED TUBE END TO COMPLETELY SEAT ON THE CONICAL SURFACE OF THE UNION FITTING DURING TORQUE APPLICATION. NO OTHER PROBLEMS WERE NOTED THAT COULD HAVE CONTRIBUTED TO THIS PROBLEM BASED ON A 100% INVENTORY STOCK CHECK, THE MISTHREADED WEBER AEROSPACE UNION FITTING (MS24392-J6) IS AN ISOLATED INCIDENT THAT IS ATTRIBUTED TO NORMAL PRODUCTION FALL OUT AS AN ENHANCEMENT THE CREW MEETING WAS HELD TO HEIGHTEN THE EMPLOYEES' AWARENESS OF THE INCIDENT TASK CLOSED THIS CAPS IS CLOSED. NO FURTHER ACTION IS REQUIRED |
| MSFC Response/Concurrence 02/04/99 - MSFC APPRVOES CLOSED WITH ACTION STATUS. THIS STATUS IS EFFECTIVE THROUGH 04/29/99 02/25/99 - MSFC APPROVES CLOSURE OF THIS CAPS |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A17359 | IFA# -- | Contractor RPT# P-087 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 11931-009 AND -019 | Asmnt Part Name ET COMPLETE | Asmnt Serial/Lot# ET - 102 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MA - MFG-ASY | FAIL MODE MV - EXT LEAK |
| Asmnt FMEA 2.4.10 | Asmnt FM .1 | FMEA CSE .1 | FMEA SCSE -- |
| Asmnt FMEA 2.4.11 | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |