SPECIFICATIONS FOR WAVEMETER- SOLICITATION 1-057-RFJ.1255

Specifications are as follows:

Pulse and continuous wavemeter

Wavelength range: 0.3 to 1.1 µm

Accuracy: 1.0 part in 10^^7 (1.0 part in 10,000,000)

Spectral resolution: 500 MHz or better

Input power range: 10 µW to 1.0 mW (µW is microWatt and mW is milliWatt)

Input energy range: 0.1 to 10.0 µJ

Operational rate: 20 Hz or better when used with Pentium PC or better

Power specifications: 100 V, single phase

Fiber optic coupler: included

PCI Interface: included

Single Frequency HeNe  : Special distribution single frequency Power output >0.1 mW