Long Island Rail Road East Side Access

New York, New York

(November 2005)

The Metropolitan Transportation Authority (MTA) and the Long Island Rail Road (LIRR) are proposing to construct a new direct 3.5-mile commuter rail extension from LIRR’s Main and Port Washington Branch Lines in Long Island and Queens, to Grand Central Terminal (GCT) on Manhattan’s East Side.  The project includes the construction of a new station in the Sunnyside area of Queens, and new tunnels beneath Sunnyside Yard connecting to the currently unused lower level of the 63rd Street Tunnel beneath the East River.  In Manhattan, the project would continue west beneath 63rd Street and towards Park Avenue under the Lexington Avenue subway, turning south beneath the existing MTA-Metro North Railroad tracks under Park Avenue to a new LIRR passenger concourse in the lower level of GCT.  At GCT, the project would provide new tracks, platforms, entrances, waiting areas, ticket windows, and other services.

The current highway system and East River crossings (bridges and tunnels) to Manhattan from Nassau/Suffolk (and parts of eastern Queens) are at capacity and subject to severe congestion and long delays.  Expansion of the highway network is not feasible due to lack of available rights-of-way, high costs, and potentially adverse environmental impacts in a “severe” non-attainment area for ozone.  The LIRR operates at capacity in this area with peak service of 37 trains per hour into its only Manhattan terminal at Penn Station.  Nearly half of LIRR’s 106,000 existing daily riders have destinations on Manhattan’s East Side, and currently spend approximately 20 minutes “doubling back” from Penn Station on the island’s West Side.  Without the project, future LIRR trains to Penn Station will be severely congested, and are projected to operate at 27 percent over their passenger-carrying capacity.  This level of crowding and discomfort would discourage or prevent new riders from using the LIRR to reach Manhattan.  By redirecting trains to GCT, this congestion would be relieved and added capacity for Amtrak and New Jersey Transit service would be created at Penn Station.

| Summary Description |
| --- |
| Proposed Project: | Commuter Rail Extension |
|  | 3.5 Miles 2 Stations |
| Total Capital Cost ($YOE): | $7,779.3 Million (includes $1.47 billion in finance charges) |
| Section 5309 New Starts Share ($YOE): | $2,632.1 Million (33.8%) |
| Annual Forecast Year Operating Cost: | $348.0 Million |
| Ridership Forecast (2030): | 171,900 Average Weekday Boardings |
|  | 27,300 Daily New Riders |
| Opening Year Ridership Forecast (2012): | 166,300 Average Weekday Boardings |
| FY 2007 Finance Rating: | Medium |
| FY 2007 Project Justification Rating: | Medium-High |
| FY 2007 Overall Project Rating: | Medium |

FTA notes that MTA/LIRR’s New Starts funding request of $2.63 billion is higher than what has historically been provided by FTA to other major transit capital investment projects, but the New Starts share (less than 34%) is significantly lower.  FTA expects to execute a Full Funding Grant Agreement (FFGA) for the Long Island Rail Road East Side Access project in FY 2006.

Project Development History and Current Status

MTA/LIRR completed a major investment study for the project corridor in April 1998.  FTA approved MTA/LIRR’s request to advance the project into preliminary engineering in September 1998.  A Draft Environmental Impact Statement (EIS) was completed in May 2000; a Final EIS was completed in March 2001; and an environmental Record of Decision was issued by FTA in May 2001.  FTA approved the project into final design in February 2002.  The project was recommended for an FFGA in the FY 2005 and 2006 President’s Budgets.  Execution of the FFGA was delayed because the MTA’s 2005-2009 capital program did not include expected revenues for the project.  MTA and State budget officials are currently solidifying financing strategies to implement the project, including the use of recently approved bond revenues.

Significant Changes Since FY 2006 Evaluation (November 2004)

In June 2005, MTA provided a revised set of travel forecasts reflecting a 2030 forecast year and updated population and employment assumptions for the New York City area.  Project finance costs increased by $40 million since last year.  In early November 2005, New York voters approved a statewide bond referendum that will provide an additional $450 million in funding to the project.

Project Justification Rating: Medium-High

The project is rated Medium-High based on a Medium rating for cost effectiveness and a High rating for transit-supportive land use.

Cost Effectiveness Rating: Medium

The Medium cost effectiveness rating reflects the level of travel-time benefits (106,200 hours each weekday) relative to the project’s annualized costs.  The estimate of both costs and benefits of the project at this stage of development is considered reliable.

| Cost Effectiveness |
| --- |
| Cost per Hour of Transportation System User Benefit Incremental Cost per Incremental Trip | New Start vs. Baseline $18.43* $36.22 |

* Indicates that measure is a component of Cost Effectiveness rating.

The East Side Access project would increase LIRR’s tunnel capacity across the East River by 50 percent and shorten daily travel time for 84,000 LIRR riders destined for Manhattan’s East Side by an estimated 40 minutes per passenger.  The redistribution of ridership from Penn Station to LIRR’s new service at GCT would significantly improve travel throughout the LIRR network.  LIRR would be able to expand peak hour service to Manhattan from 37 trains to a projected 61 trains (a 40 percent increase), with 24 peak hour trains serving GCT.  Approximately 70 percent of daily travel-time benefits would result from LIRR riders no longer traveling in overcrowded conditions between parts of Queens, all of Nassau and Suffolk counties, and Manhattan.  The remaining travel time benefits are experienced by LIRR riders who will no longer have to retrace their route to reach destinations on Manhattan’s East Side near GCT, and those who encounter less crowded conditions at Penn Station on Manhattan’s West Side.

The project has been sufficiently developed to the point that the definition of the scope is firm.  However, since several critical path items (award of Manhattan and Queens tunnel excavation contracts and an executed Amtrak operating agreement) did not occur as planned, the current schedule for revenue operations (2012) is being reevaluated.  Inflation assumptions for capital costs should also be reexamined.  FTA is working with MTA to update the project’s risk analysis/risk mitigation program to manage the technical work and reduce project uncertainties.

Transit-Supportive Land Use Rating: High

The High land use rating is based upon the High ratings assigned to all of the subfactors as summarized below.

Existing Land Use: High

- The Grand Central Terminal is located in a uniquely high-intensity setting where transit and walking are the dominant modes of transportation.  Nearly 660,000 employees work within ½ mile of the station, and over 50,000 people reside within this same area.

- Land use in the Sunnyside station area is currently industrial, although the Queens Plaza transportation hub, directly to the north of the yard, has a station serving six subway lines, and thus generates substantial pedestrian activity.  Redevelopment of the areas northwest and south of the railroad complex is underway.  Over 25,000 employees currently work in the Sunnyside station area, which houses a residential population of 9,300.

- The character of development is highly pedestrian-oriented in the GCT station area.  While existing land use at the site of the proposed Sunnyside station area does not currently create an attractive pedestrian environment, there is significant pedestrian traffic in the area due to the presence of several subway connections at Queens Plaza and pockets of redevelopment to the northwest (Court Square) and south of the railroad complex.

- New York City discourages parking in the central business district (CBD) by leveraging an 18 percent tax on off-street parking in Manhattan.  Off-street parking is available in the GCT area, but parking costs are extremely high, typically upwards of $25 per day.

Transit-Supportive Plans and Policies: High

- Building density on the East Side of Midtown Manhattan near the GCT area is exceptionally high, and city policies encourage neighborhood preservation, the continued concentration of activity in the area, and investment in pedestrian facilities.  An increase of 70,000 workers and 7,000 residents is projected in the GCT area by 2025.

- New York City plans to create a new central business district within the Sunnyside station area by promoting intensification of office, residential, and institutional development.  Zoning revisions have recently been adopted to implement these plans.  It is anticipated that the dense urban environment combining industrial, commercial, institutional, and residential uses that will be created will be more typical of transit-oriented development than the existing, predominantly industrial, landscape.  Employment in the Sunnyside station area is projected to grow by 3,500, while population is estimated to increase by 1,200 by 2025.

- New York City’s development plan for the Sunnyside area includes four million additional square feet of office space within walking distance of the proposed station.

- Policies in New York City, Nassau County and Suffolk County support the concentration of new development in existing centers.

Performance and Impacts of Policies: High

- Several examples of transit- and pedestrian-friendly improvements implemented in conjunction with new private development illustrate the effectiveness of city land use policies.  A 45-story Bear Stearns headquarters building is nearing completion along Madison Avenue and will include ground floor retail uses and escalators leading to cross passageways serving the platforms at GCT.  A major insurance company, Met Life, has moved its corporate headquarters to the Sunnyside station area at Queens Plaza North and is building an adjacent tower.

- Recent zoning changes have resulted in development of a new commercial hub proposal between the Queens Plaza subway station adjacent to the proposed Sunnyside station and the Court Square office district.

Other Project Justification Criteria

| Mobility Improvements Rating: High |
| --- |
| Within ½-mile radius of boarding areas: Existing Employment Projected Employment (2030) Low Income Households (% of total HH) Average Per Station: Employment Low Income Households Transportation System User Benefit Per Project Passenger Mile (Minutes) | 697,700 828,600 3,130 (8%) 348,900* 1,600* New Start vs. Baseline 11.05* |
| Environmental Benefits Rating: High |
| Criteria Pollutant (Reduction in tons) Carbon Monoxide (CO) Nitrogen Oxide (NOx) Volatile Organic Compounds (VOC) Particulate Matter (PM10) Carbon Dioxide (CO2) Criteria Pollutant Status Carbon Monoxide (CO) 8-Hour Ozone (O3) Particulate Matter (PM10) Particulate Matter (PM2.5) Annual Energy Savings (million British Thermal Units) | New Start vs. Baseline 1,470 40 30 30 36,900 EPA Designation Maintenance Area* Moderate Non-Attainment Area* Moderate Non-Attainment Area* Non-Attainment Area* 418,800 |
| Operating Efficiencies Rating: Medium |
| System Operating Cost per Passenger Mile (current year dollars) | Baseline $0.295* | New Start $0.299* |

* Indicates that measure is a component of rating for each criterion.

N/A indicates information was not available for this entry.

# Local Financial Commitment Rating: Medium

The Medium local financial commitment rating is based on the High rating for the New Starts share of project costs and the Medium ratings for both the capital and operating finance plans.

Section 5309 New Starts Share of Total Project Costs: 34%

Rating: High

MTA/LIRR is requesting a 34 percent New Starts share of total project costs, which results in a High rating for this measure.

| Locally Proposed Financial Plan |
| --- |
| Source of Funds | Total Funds ($million) | Percent of Total |
| Federal: Section 5309 New Starts Flexible Funds (CMAQ) Other Federal | $2,632.1 $11.2 $28.2 | 33.8% 0.1% 0.4% |
| State: State Transportation Bond Act of 2005 | $450.0 | 5.8% |
| Local: MTA Dedicated Sources (bonds, surplus toll revenues, etc.) MTA Operating Budget | $3,184.2 $1,473.6 | 40.9% 18.9% |
| Total: | $7,779.3 | 100.0% |

NOTE:  The financial plan reflected in this table has been developed by the project sponsor and does not reflect a commitment by DOT or FTA.  The sum of the figures may differ from the total as listed due to rounding.

# Capital Finance Plan Rating: Medium

The capital finance plan is rated Medium, based upon the average of the ratings assigned to each of the subfactors listed below.  The capital condition, completeness of the plan, commitment of funds and the capital cost estimate and planning assumptions subfactors were rated Medium.  The capital funding capacity subfactor was rated Medium-Low.

#### Agency Capital Condition: Medium

- The average age of MTA’s bus fleet is 6.1 years, which is near the industry average.  The average age of the MTA’s rail fleet is 19.8 years for New York City Transit and 19.9 years and 19.0 years for the LIRR and Metro-North Railroad, respectively.

- MTA’s bond ratings, which were issued in March 2000, are as follows: Standard & Poor’s AA- and Fitch A+.

#### Completeness of Capital Plan: Medium

- The financial plan included a 20-year cash flow statement, more than five years of historical data, identification of some key assumptions with little detail, supporting documentation including fleet management plans, and a limited sensitivity analysis.

#### Commitment of Capital Funds: Medium

- Approximately 62 percent of non-New Starts funding is committed or budgeted.  Primary funding sources include bond proceeds, State and local capital support, and other dedicated tax revenues.

#### Capital Funding Capacity: Medium-Low

### The financial plan shows a balanced budget, with no cash surpluses beyond 2005.  MTA has limited reserve accounts and/or access to credit that would allow MTA to cover cost increases or funding shortfalls.

#### Capital Cost Estimate and Planning Assumptions: Medium

### Assumptions in the capital plan are consistent with historical experience.

### There is concern about maintaining the project schedule, which would likely have an effect on the capital cost estimate.

#### Operating Finance Plan Rating: Medium

The operating finance plan is rated Medium, based upon the average rating of the five subfactors listed below.  A High rating was assigned for the commitment of operating funds subfactor.  The completeness and operating cost estimates and planning assumptions subfactors were rated Medium.  The agency operating condition and operating funding capacity were rated Medium-Low.

#### Agency Operating Condition: Medium-Low

- MTA is in fair financial condition.  Except for the service interruptions resulting from the September 11th attacks, MTA has not reduced service in recent years.

- MTA’s current ratio of assets to liabilities as reported in its most recent audited financial statement is 1.02.

#### Completeness of Operating Plan: Medium

- The financial plan included a 20-year cash flow statement, more than five years of historical data, the identification of some assumptions with little detail, supporting documentation and no sensitivity analysis.  There were inconsistencies between the financial plan narrative, the financial plan cash flow statement and the adopted and proposed MTA multi-year budgets.

#### Commitment of Operating Funds: High

- Over 92 percent of operating funding is committed.  The remainder is considered budgeted.  Funding sources include fares, other operating revenues, and dedicated State and local taxes.

#### Operating Funding Capacity: Medium-Low

- The financial plan does not show cash balances or reserve accounts because MTA is required to operate under a balanced budget by statute.  Consequently, MTA’s financial plan indicates that operating sources will be equal to operating uses for the period 2005–2024.  MTA has access to short-term credit exceeding 8 percent of annual operating expenses.

#### Operating Cost Estimates and Planning Assumptions: Medium

- Operating cost estimates and revenue forecasts are consistent with historical trends.

Map